## Slide 1: Homelab Tiva™ C Series TM4C123G LaunchPad
Authors:
Vittoriano Muttillo
Walter Tiberti
Embedded Systems: Tiva TM4C123G Homelab
Notes: This workshop has been constructed to be extensively hands-on, and the overwhelming majority of your time will be spent working with the tools and writing code. If you don't already have some experience with embedded microcontrollers and using the C programming language, you need to acquire that experience before proceeding. There are many resources online that you can use to obtain that knowledge.
In case you didn't know it already, this workshop is available at http://www.ti.com/TM4C123G-Launchpad-Workshop. That wiki site has links to all of the material you need to run this workshop.

## Slide 2: Agenda
Embedded Systems: Tiva TM4C123G Homelab
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Summary of seminar’s Agenda

## Slide 3: Tiva™ EK-TM4C123GXL LaunchPad
ARM® Cortex™-M4F 64-pin 80MHz TM4C123GH6PM
On-board USB ICDI (In-Circuit Debug Interface)
Micro AB USB port
Device/ICDI power switch
BoosterPack XL pinout also supports legacy BoosterPack pinout
2 user pushbuttons (SW2 is connected to the WAKE pin)
Reset button
3 user LEDs (1 tri-color device)
Current measurement test points
16MHz Main Oscillator crystal
32kHz Real Time Clock crystal
Support for multiple IDEs:
Embedded Systems: Tiva TM4C123G Homelab
Notes: The TM4C123GXL LaunchPad board has some impressive features for a small price. The onboard processor is a Texas Instruments Tiva C Series TM4C123GH6PM microcontroller. It's a member of the ARM Cortex M4F family with 64 pins and has a top speed of 80 megahertz. The LaunchPad has two USB ports, one at the top for emulation and one of the left side as a OTG/Host and Device user port. The board can be powered through either port using the power switch in the upper left.
There are two user push buttons at the bottom of the board. The one on the right is also connected to the wake pin on the microcontroller that will wake it from hibernation mode. A reset button is provided in the emulator area of the board in the upper right.
Just below the reset button is a tricolor LED that combines the red, green, and blue LEDs into a single package. To the right of the device USB port are two test points where you can measure the current draw of the microcontroller. They are connected by a jumper.
There are two crystals on the board, a 16MHz one that drives the main oscillator and a 32,768-hertz one that drives the real-time clock oscillator. Since many computer USB ports can deviate significantly from 3.3 volts, an onboard voltage regulator is provided.
Expandability is an important aspect of all TI's LaunchPad boards. The Tiva LaunchPad features the booster pack XL pin out, which offers additional signals while still supporting existing booster packs.
All Tiva C Series devices offer support for multiple integrated development environments or IDEs. Mentor graphics, mentor-embedded, source recode bench, IAR systems embedded workbench, ARM, Keil Microvision IDE, and Texas Instruments Code Composer Student are all supported. Code Composer Studio, or CCS, will be our tool of choice in this workshop.

## Slide 4: Tiva™ TM4C123G Microcontroller
Low power consumption
As low as 370 µA/MHz
500µs wakeup from low-power modes
RTC currents as low as 1.7µA
Internal and external power control
Embedded Systems: Tiva TM4C123G Homelab
Notes: Tiva C Series microcontrollers have a wide range of peripherals and capabilities. In the figure on the left-hand side, we can see the ARM Cortex M4F core, which supports JTAG access, as well as serial wire debug for testability.
Within the M4F is the NVIC or Nested Vectored Interrupt Controller, the MPU or memory protection unit and the FPU or floating point unit. ETM is the embedded trace macrocell for extended testing on the device.
The TM4C123H6PM device has 256K of flash, 32K of SRAM, 2K of EEPROM and an onboard ROM. I'll talk about the ROM contents in a moment..
On the analog side, there is a LDO voltage regulator for regulating the CPU voltage on the device, and 3 analog comparators. There are two, 1Msps 12-bit ADCs. 24 input channels are connected through 12 shared inputs on this device and there is an onboard temperature sensor.
On the lower left are the serial interfaces. As many as eight UARTs, four SSI or SPI ports, a USB Host/Device and On-the-Go port, 2 CAN ports, or as many as 6 I2C ports. In each case I said “as many as” because most of the 64-pins on this device are heavily multiplexed and the number of peripherals that reach the pins will be determined by your decision with regard to that.
In the lower middle are the motion control modules. These modules provide 16 PWM outputs with dead band generation for H bridge circuitry protection . Two quadrature encoder inputs are included .
On the lower right are the clocks, reset and system control . The clock tree is very flexible on these devices . Below that is the SysTick timer which can be used as a general-purpose timer or as the heartbeat timer for an operating system. Below that are the 12 general-purpose timers . These can be configured for PWM or capture and compare purposes . They can also be flexibly set up as 16, 32 or 64 bit timers . There are two watchdog timers , each on a separate clock source . As many as 43 general-purpose I/O and a 32 channel DMA .There is a internal precision oscillator requiring no external components and a hibernate module that includes a Real-Time clock and battery-backed SRAM .
These parts have power consumption as low as 370 microamps per megahertz, 500 microseconds wake-up from low power modes, and realtime clock currents as low as 1.7 microamps. Power control is provided for both internal and external circuitry .

## Slide 5: M4 Core and Floating-Point Unit
32-bit ARM® Cortex™-M4 core
Thumb2 16/32-bit instruction set
System clock frequency up to 80 MHz
100 DMIPS @ 80MHz
Flexible clocking system
  Internal precision oscillator
  External main oscillator with PLL support
  Internal low frequency oscillator
  Real-time-clock through Hibernation module
Atomic bit manipulation. Read-Modify-Write using bit-banding
Single Cycle multiply and hardware divider
IEEE754 compliant single-precision floating-point unit
JTW and Serial Wire Debug debugger access
  ETM (Embedded Trace Macrocell) available through Keil and IAR emulators
Embedded Systems: Tiva TM4C123G Homelab
Notes:   Tiva C series devices are built with a 32 bit ARM Cortex – M4 core. This core runs the Thumb2 instruction set. This instruction set uses both 16 and 32-bit instructions.
  With a clock frequency of up to 80 MHz the core delivers 100 DMIPS at 80 MHz . The part has a very flexible clocking system with an internal precision oscillator , an external main oscillator with PLL support , an internal low-frequency oscillator and a Real-Time clock through the hibernation module .
  For signal processing applications the core implements saturated math instructions . Read – modify – write operations are atomic and use the bit banding technique that we’ll cover later .
  There is a single cycle multiply and a hardware divider. Data access is unaligned for more efficient memory usage .
  The single-precision floating point unit is IEEE–754 compliant . JTAG and serial wire debug debugger access is provided.

## Slide 6: TM4C123GH6PM Memory
256KB Flash memory
  Single-cycle to 40MHz
  Pre-fetch buffer and speculative branch improves performance above 40 MHz
32KB single-cycle SRAM with bit-banding
Internal ROM loaded with TivaWare software
  Peripheral Driver Library
  Boot Loader
  Advanced Encryption Standard (AES) cryptography tables
  Cyclic Redundancy Check (CRC) error detection functionality
2KB EEPROM (fast, saves board space)
  Wear-leveled 500K program/erase cycles
  Thirty-two 16-word blocks
  Can be bulk or block erased
  10 year data retention
  4 clock cycle read time
0x00000000 Flash
0x01000000 ROM
0x20000000 SRAM
0x22000000 Bit-banded SRAM
0x40000000 Peripherals & EEPROM
0x42000000 Bit-banded Peripherals
0xE0000000 Instrumentation, ETM, etc.
Embedded Systems: Tiva TM4C123G Homelab
Notes: There are four different kinds of memory on this device .
The 256 KB flash memory is single-cycle to 40 MHz . A pre-fetch buffer and speculative branching improves performance above 40 MHz .
The 32 KB single-cycle SRAM implements bit-banding that we will cover later .
The internal ROM is loaded with the TivaWare Peripheral driver library , the boat loader, cryptography tables and CRC error detection functionality.
The 2 KB EEPROM is wear-leveled to provide 500,000 program and erase cycles with a five year data retention. Random access requires four clock cycles while sequential access is single-cycle for each location after the first .
Note the figure on the lower right with flash memory starting out at zero , followed by ROM, SRAM , the bit-banded alias of the SRAM , peripherals and EEPROM , followed by the bit-banded alias of the peripherals and finally some additional locations.

## Slide 7: TM4C123GH6PM Peripherals (1)
Battery-backed Hibernation Module
  Internal and external power control (through external voltage regulator)
  Separate real-time clock (RTC) and power source
  VDD3ON mode retains GPIO states and settings
  Wake on RTC or Wake pin
  Sixteen 32-bit words of battery backed memory
  5 µA Hibernate current with GPIO retention. 1.7 µA without
Serial Connectivity
  USB 2.0 (OTG/Host/Device)
  8 - UART with IrDA, 9-bit and ISO7816 support
  6 - I2C
  4 - SPI, Microwire or TI synchronous serial interfaces
  2 - CAN
Embedded Systems: Tiva TM4C123G Homelab
Notes:   The part is equipped with a battery backed hibernation module . This module provides internal and external power control with the use of a external voltage regulator . The hibernation module supplies a separate real-time-clock and a battery power source . The VDD3ON mode retains the states of the external pins during hibernation to prevent errors or damage to external circuitry. Waking from hibernation can be done on a Real-Time clock match or by toggling the wake pin. 16 32 bit words of battery-backed SRAM are provided within the hibernation module . When configured for GPIO retention hibernation current is 5uA. Without GPIO retention and with the Real-Time clock running it is 1.7 uA.
  Serial connectivity to the part is provided through a USB 2.0 OTG/Host/Device port, eight UART ports, six I2C ports, four Synchronous Serial ports and two CAN ports .

## Slide 8: TM4C123GH6PM Peripherals (2)
Two 1MSPS 12-bit SAR ADCs
  Twelve shared inputs
  Single ended and differential measurement
  Internal temperature sensor
  4 programmable sample sequencers
  Flexible trigger control: SW, Timers, Analog comparators, GPIO
  VDDA/GNDA voltage reference
  Optional hardware averaging
  3 analog and 16 digital comparators
  µDMA enabled
0 - 43 GPIO
  Any GPIO can be an external edge or level triggered interrupt
  Can initiate an ADC sample sequence or µDMA transfer directly
  Toggle rate up to the CPU clock speed on the Advanced High-Performance Bus
  5-V-tolerant in input configuration (except for PB0/1 and USB data pins when configured as GPIO)
  Programmable Drive Strength (2, 4, 8 mA or 8 mA with slew rate control)
  Programmable weak pull-up, pull-down, and open drain
Embedded Systems: Tiva TM4C123G Homelab
Notes:   There are two 1Msps 12-bit successive approximation analog-to-digital converters on the device . These two ADCs share 12 inputs and can make single-ended and differential measurements . There is an internal temperature sensor and four programmable ADC sample sequencers . Flexible trigger control allows you to start a conversion sequence with software, the timers , the analog comparators or with an external pin. Because of the device’s low pin count, only the VDDA to GNDA voltage reference is provided . There is optional hardware averaging , two analog and 16 digital comparators. DMA support is provided.
  The device has as many as 43 GPIO depending on which peripherals you choose to bring out to the pins . Any GPIO can be an external edge or level triggered interrupt and can directly initiate an ADC sample sequence or DMA transfer.The toggle rate can be as high as the CPU clock speed when using the advanced high-performance bus . Inputs are 5V tolerant (with a few exceptions) and the drive strength of the outputs can be programmed to 2, 4, and 8mA. The 8mA setting provides slew rate control. All GPIO have programmable weak pull-up , pull-down and open-drain options .

## Slide 9: TM4C123GH6PM Peripherals (3)
Memory Protection Unit (MPU)
  Generates a Memory Management Fault on incorrect access to region
Timers
  2 Watchdog timers with separate clocks
  SysTick timer. 24-bit high speed RTOS and other timer
  Six 32-bit and Six 64-bit general purpose timers
  PWM and CCP modes
  Daisy chaining
  User enabled stalling on CPU Halt flag from debugger for all timers
32 channel µDMA
  Basic, Ping-pong and scatter-gather modes
  Two priority levels
  8,16 and 32-bit data sizes
  Interrupt enabled
Notes: The memory protection unit or MPU provides up to 64 memory regions on the device that can be configured for access control . Incorrect access to one of these regions will generate a memory management fault .
There are two watchdog timers with separate clocks in case one of them fails , a 24 bit SysTick high-speed general-purpose or RTOS timer and six 32-bit and six 64-bit general-purpose timers . The general-purpose timers have PWM and capture and compare modes as well as daisy chaining. Timers can be configured to stall when the processor is halted by the debugger .
A 32 channel DMA provides basic, ping-pong and scatter gather modes with two priority levels . Data sizes can be 8, 16 and 32 bit. The DMA is interrupt enabled.

## Slide 10: TM4C123GH6PM Peripherals (4)
Nested-Vectored Interrupt Controller (NVIC)
  7 exceptions and 71 interrupts with 8 programmable priority levels
  Tail-chaining and other low-latency features
  Deterministic: always 12 cycles or 6 with tail-chaining
  Automatic system save and restore
Two Motion Control modules. Each with:
  8 high-resolution PWM outputs (4 pairs)
  H-bridge dead-band generators and hardware polarity control
  Fault input for low-latency shutdown
  Quadrature Encoder Inputs (QEI)
  Synchronization in and between the modules
Embedded Systems: Tiva TM4C123G Homelab
Notes: The nested Vectored interrupt controller offers 7 system level exceptions and 65 interrupts with 8 programmable priority levels . The majority of the interrupts in the vector table can be re-programmed two any of these eight priority levels . Asynchronous interrupt latency is reduced through the use of a feature called tail chaining . Response is deterministic : it is always 12 cycles or six cycles when tail chaining is used . System save and restoration is completely automatic .
The device has two motion control modules . Each module has 8 high resolution PWM outputs configured in 4 pairs . Dead band generators and hardware polarity control make it easy to drive H bridge circuitry . Dedicated fault inputs allow low latency shutdown . System feedback is done using Quadrature encoder inputs . The motion control modules can operate independently or can be synchronized .

## Slide 11: Agenda
Embedded Systems: Tiva TM4C123G Homelab
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter two is an introduction to Developments tools

## Slide 12: Development Tools for Tiva C Series MCUs
Eval Kit License | 30-day full function. Upgradeable | 32KB code size limited. Upgradeable | 32KB code size limited. Upgradeable | Full function. Onboard emulation limited | Open-source electronics prototyping platform
Compiler | GNU C/C++ | IAR C/C++ | RealView C/C++ | TI C/C++ | GNU C/C++ (MSPGCC)
Debugger / IDE | gdb / Eclipse | C-SPY / Embedded Workbench | µVision | CCS/Eclipse-based suite | Processing
Full Upgrade | 99 USD personal edition / 2800 USD full support | 2700 USD | MDK-Basic (256 KB) = €2000 (2895 USD) | 445 USD | FREE
JTAG Debugger |  | J-Link, 299 USD | U-Link, 199 USD | XDS100, 79 USD | 
Notes: 12
12
12
Tiva C Series microcontrollers are supported by five different integrated development environments: Mentor graphics Mentor-Embedded, IAR systems Embedded Workbench, ARM Keil Microvision, Texas Instruments Code Composer Studio and Energia.
Each company offer different evaulation licenses. Some are code-size limited and others are time limited. Code Composer Studio is full function, but it's onboard emulation limited. When connected to the LaunchPad board it is fully functional and free. Only if you connect CCS to a target board will you need to buy it.
Some companies use the GNU compiler, while others use their own. TI’s compiler has been developed in-house over many years.
For the debugger and editor interface, two of the tools offer Eclipse support. Eclipse is an open source tool that is quite popular at this time, primarily because of the many third party tools available as add-ins.
The prices for upgrading to the full versions are shown in the chart. Code Composer Studio is $445US for the downloaded version. If you want the CD, it's $495US.
Most of the companies offer JTAG debuggers, and there are also quite a few third-party debuggers for sale as well.

## Slide 13: TI Software and Tools Ecosystem
  High-level OS support and TI-RTOS
  OS Independent support and TI-Wares software packages
Run-Time Software
Development Tools
  TI Design Network: off-the-shelf software, tools and services
  Forums & Wikis
  In-person and online training
Support & Community
  CCStudio™ Integrated Development Environment (IDE) and other IDEs
  Optimizing compilers
  Design Kits & Evaluation Modules
Embedded Systems: Tiva TM4C123G Homelab
Notes: Development tools like Code Composer and evaluation products like the LaunchPad board are just a part of TI’s support ecosystem for it’s processors.
Run-time software support includes TivaWare for C Series as well as TI’s RTOS called SysBios.
There is a rich community of support for TI’s products through the forums, e2e pages, Wikis, in-person and on-line training.

## Slide 14: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter three is an introduction to install driver and software tools

## Slide 15: Hardware and Software Setup
Connect HW
Install Driver
Install Code Composer Studio™
TivaWare™ and other programs
Test QuickStart Application
USB Emulation Connection
Embedded Systems: Tiva TM4C123G Homelab
Notes: In chapter three, you'll obtain and install all the needed hardware and software, as well as test out the pre-installed application software on the LaunchPad board.

## Slide 16: Install Driver
Stellaris In-Circuit Debug Interface (ICDI)
Tiva™ C Series design kits provide Stellaris In-Circuit Debug Interface (ICDI)
which allows programming and debugging LM4F microcontroller
The Stellaris ICDI can be used with the LM Flash Programmer
Only JTAG is supported
Stellaris ICDI Drivers
To debug and download the custom application in the microcontroller’s Flash
memory and use Virtual COM Port connectivity, install the following drivers:
  Stellaris Virtual Serial Port
  Stellaris ICDI JTAG/SWD Interface
  Stellaris ICDI DFU
These drivers provide the debugger with access to the JTAG interface and the
host PC with access to the Virtual COM Port
Driver installation
Windows XP/7/8 http://www.ti.com/tool/stellaris_icdi_drivers#descriptionArea
Windows 10 is supported, but there isn’t feedback by TI at this moment
Embedded Systems: Tiva TM4C123G Homelab
Notes: DRIVER

## Slide 17: Install Code Composer Studio
Download
For download register and logging in TI web site:
  http://www.ti.com/
Download and start the latest version of Code Composer Studio (CCS) 6.x
from http://processors.wiki.ti.com/index.php/Download_CCS (no beta)
  web installer (will require Internet access until it completes)
  offline version (much larger than web installer)
Install
Launch the ccs_setup_6.xxxxx.exe file
Accept the Software License Agreement and click Next
Accept the default installation folder and click Next
Select “Custom” for the Setup type and click Next
select the processors that CCS will support (select “Tiva C Series ARM MCUs”)
In the Component dialog, keep the default selections and click Next
In the Emulators dialog, uncheck the Blackhawk and Spectrum Digital
emulators, unless you plan on using either of these and click Next
When you reach the final installation dialog click Next and wait
Installation will succeed after waiting a while
Embedded Systems: Tiva TM4C123G Homelab
Notes: INSTALL CCS

## Slide 18: TivaWare™ and other programs (1)
TivaWare™ for C Series
Software suite tools to speed development of Tiva C Series MCU applications
Download and install the latest full version of TivaWare from:
  http://www.ti.com/tool/sw-tm4c
The filename is SW-TM4C-x.x.exe and install TivaWare into the default folder:
C:\TI\TivaWare_C_Series-x.x folder
LM Flash Programmer
Free flash programming utility
Download, unzip and install the latest LM Flash Programmer from:
  http://www.ti.com/tool/lmflashprogrammer
Workshop Lab Files
Download and install the lab installation file from:
  http://www.ti.com/TM4C123G-Launchpad-Workshop
The file will install your lab files in:
  C:\Tiva_TM4C123G_LaunchPad
Embedded Systems: Tiva TM4C123G Homelab
Notes: TivaWare Install

## Slide 19: TivaWare™ and other programs (2)
Workshop Workbook
Download a copy of the workbook pdf file from the workshop materials section
of the Wiki site below to your desktop from:
  http://www.ti.com/TM4C123G-Launchpad-Workshop
Terminal Program
PuTTY: http://www.chiark.greenend.org.uk/~sgtatham/putty/download.html
Other terminal emulators
Helpful Documents and Sites
Helpful documents in in C:\TI\TivaWare_C_Series-1.1\docs
TM4C123GH6PM Microcontroller Data Sheet
Main page: www.ti.com/launchpad
Tiva C Series TM4C123G LaunchPad: http://www.ti.com/tool/ek-tm4c123gxl
TM4C123GH6PM folder: http://www.ti.com/product/tm4c123gh6pm
BoosterPack webpage: www.ti.com/boosterpack
LaunchPad Wiki: www.ti.com/launchpadwiki
Embedded Systems: Tiva TM4C123G Homelab
Notes: Workbook and others

## Slide 20: Test QuickStart Application
Connect LaunchPad Board and test Quickstart Application (Example CCS folder)
Turn power switch in the upper left corner in the right DEBUG position
Software uses the timers as pulse-width modulators (PWMs) to vary the
intensity of all three colors on the RGB LED (red, green, and blue) individually
Functionalities
Two pushbuttons at the bottom of board are marked
  SW1 (the left one)
  SW2 (the right one)
Press and/or hold SW1 to move towards the red-end of the color spectrum
Press and/or hold SW2 to move towards the violet-end of the color spectrum
If no button is pressed for 5 seconds, the software returns to automatically
changing the color display
Press and hold both SW1 and SW2 for 3 seconds to enter hibernate mode
Pressing SW2 at any time will wake the device and return to automatically
changing the color display.
The system can also be controlled via a command line provided via the UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Quickstart Application

## Slide 21: Agenda
Embedded Systems: Tiva TM4C123G Homelab
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter four is an introduction to Code Composer Studio Version 5.x. Code Composer Studio is an Integrated Development Environment, or IDE, that combines editing, debugging, and analysis tools into a single package. It's based on the Eclipse open source development tool. Before you can write code for the Tiva C Series device, you need to get acquainted with the tool you'll be using.

## Slide 22: Code Composer Studio Functional Overview
Compiler
Assembler
Linker
.c
.asm
.obj
.asm
Edit
Debug
Simulator
Emulator/ LaunchPad
Target Config File
Integrated Development Environment (IDE) based on Eclipse
Contains all development tools – compilers, assembler, linker, debugger, BIOS and includes one target – the Simulator
GEL files initialize the debugger so that it understands where memory, peripherals, etc. are
Standard Runtime Libraries
.lib
.map
User.cmd
SYS/BIOS
Libraries
SYS/BIOS
Config
(.cfg)
Bios.cmd
.out
.ccxml
Stand-Alone Emulator
Target Board
. . .
.gel
Embedded Systems: Tiva TM4C123G Homelab
Notes: Code composer studio is an integrated development environment . This means that it contains the tools necessary to create , compile and debug software on your design .
CCS is based on the open source eclipse platform and is quite flexible and expandable .
A normal development flow would be to create C source files using the editor on the left . These files would then be compiled to create assembly files which are then assembled into relocatable object files . These object files, along with any libraries that you may include are linked into an output file using the guidance provided by the command file . The command file contains a list of all memories on the part, and what types of software should be placed within them .
Finally the debugger on the right uses the target configuration file and gel startup files to initialize and load your software onto your target device .
Code composer contains a simulator On which you can test your software . Evaluation boards like the launchpad contain their own built in emulator to connect CCS to the hardware . For target boards that do not contain an emulator , like any normal customers design , a stand-alone emulator must be provided . There are many available from TI and other third parties .

## Slide 23: Target Configuration and Emulators
The Target Configuration File specifies:
Connection to the target (Simulator or Emulator type)
Target device
GEL file (if applicable) for hardware setup
Emulator (Connection) Options
Built-in and external emulators from TI, Blackhawk, Spectrum Digital and others
XDS100v1/v2, 200, 510, 560, 560v2
Embedded Systems: Tiva TM4C123G Homelab
Notes: The target configuration file specifies the connection to your target . This target can be this emulator , and evaluation board /emulator combination Or a stand-alone emulator connected to a target .
The target device and the Emulator to be used must be specified .
If applicable , gel files can be used to initialize the hardware setup .

## Slide 24: Projects and Workspaces (viewed in CCS)
WORKSPACE
PROJECT
Source
Embedded Systems: Tiva TM4C123G Homelab
Notes: In eclipse, designs are organized into workspaces and projects .
This view in code composer studio is of the project explorer window . When you start code composer it will ask you what workspace you will be working in . The contents of that workspace will be shown in the project explorer window .
You can have many projects within the workspace and open and close them at will . The project explorer will show you the contents of the workspace and of the projects .

## Slide 25: Projects and Workspaces
PROJECT folder contains:
Build and tool settings (for use in managed MAKE projects)
Files can be linked to or reside in the project folder
Deleting a linked file within the Project Explorer only deletes the link
Workspace
Project 1
Project 2
Project 3
Settings/preferences
Project
Source Files
Header Files
Library Files
Build/tool settings
Source Files
Code and Data
Header Files
Declarations
Library Files
Code and Data
Link
Link
Link
Link
WORKSPACE folder contains:
IDE settings and preferences
Projects can reside in the workspace folder or be linked from elsewhere
When importing projects into the workspace, linking is recommended
Deleting a project within the Project Explorer only deletes the link
Embedded Systems: Tiva TM4C123G Homelab
Notes: This is a conceptual view of Workspaces and projects . Physically , both of these are merely folders on your computer .
The workspace folder contains code composer settings and preferences and projects that reside inside the workspace folder or that are linked from elsewhere . When you delete a linked project using project explorer , only the link will be deleted . When you delete a copied project using project explorer , the actual project will be deleted . Settings made at the workspace level effect all projects in the workspace
The project folder contains the build and tool settings for each project . Again files can be linked to or reside in the project folder . Deleting a linked file within the project explorer only deletes the late . A project can contain source files , which includes code and data, header files for declarations , library files and other settings .

## Slide 26: Creating a New Project
File New CCS Project
(in Edit perspective…)
Project Location
Default = workspace
Manual = anywhere you like
Project templates
Empty
Empty but with a main.c
Assembly only
BIOS
others
Connection
If target is specified, user can choose “connection” (i.e. the target configuration file)
Embedded Systems: Tiva TM4C123G Homelab
Notes: To create a new project in code composer studio select file, new, CCS project from the menu bar . You’ll need to define the project location . This can be inside the workspace folder , or anywhere you like on the drive .
You then need to specify the connection to the target and the device that will be used . This information is used to create the target configuration file .
You can select from a number of project templates ; empty ones , empty but with a main template , an assembly project , a bios project and other example templates .

## Slide 27: Adding Files to a Project
Users can ADD (copy or link) files into their project
SOURCE files are typically COPIED
LIBRARY files are typically LINKED (referenced)
1
Right-click on project and select:
2
Select file(s) to add to the project:
3
Select “Copy” or “Link”
COPY
Copies file from original location to project folder (two copies)
LINK
References (points to) source file in the original folder
Can select a “reference” point – typically PROJECT_LOC
Embedded Systems: Tiva TM4C123G Homelab
Notes: When you add files to your projects , you can either copy or link them . Source files are typically copied , while library files are typically linked or referenced.
To add a file to your project just for I click on the project name and select add files . You can then select the file or files that you want to add to the project . In the final step you decide whether a not to copy or link to the files . Copying will simply copy the file from its original location to the project folder . Linking references of source file in its original folder . You can select the link type whether relative to the project workspace or so on.

## Slide 28: Portable Projects
Why make your projects “portable”?
Simplifies project sharing
You can easily re-locate your projects
Allow simple changes to link to new releases of software libraries
Copied files are not a problem (they move with the project folder)
Linked files may be an issue. They are located outside the project folder via a:
  absolute path, or
  relative path
This is the Path Variable for a relative path. This can be specified for every linked file.
Embedded Systems: Tiva TM4C123G Homelab
Notes: It is important to make your projects portable . Portable projects simplify the sharing of your work with colleagues or support staff . It makes it easier to relocate your project , if desired and when software libraries are updated , it is a simple change to link to them .
In the top figure , you can see that copied files are not a problem since they will move along with the project folder . Link files on the other hand may be an issue since they are located outside the project folder and are referenced by either an absolute or relative paths .
Note the path variable in the bottom figure for the relative paths, this is specified for every linked file .

## Slide 29: Path Variables and Build Variables
Path Variables
Used by CCS (Eclipse) to store the base path for relative linked files
Example: PROJECT_LOC is set to the path of your project, say c:/Tiva_LaunchPad_Workshop/lab2/project
Used as a reference point for relative paths, e.g. ${PROJECT_LOC}/../files/main.c
Build Variables
Used by CCS (Eclipse) to store base path for build libraries or files
Example: CG_TOOL_ROOT is set to the path for the code generation tools (compiler/linker)
Used to find #include .h files, or object libraries, e.g. ${CG_TOOL_ROOT}/include or ${CG_TOOL_ROOT}/lib
How are these variables defined?
The variables in these examples are automatically defined when you create a new project (PROJECT_LOC) and when you install CCS with the build tools (CG_TOOL_ROOT)
What about TivaWare or additional software libraries? You can define some new variables yourself
Embedded Systems: Tiva TM4C123G Homelab
Notes: Two different kinds of variables are used ; path and build .
Path variables are used by CCS to store the base path for relative linked files . So the PROJECT_L OC Variable is set to the location of your project and can be used as a reference point for any other relative paths .
Build variables are used by CCS the store the base path for build libraries or files . CG_TOOL_ROOT is set to the path for the code generation tools which are the compiler and the linker. This is used to find your header files and any other object libraries.
These two variables are automatically defined when you create a new project and when you install code composer with the build tools .
TivaWare and any additional support libraries will require you to create some new variables yourself .

## Slide 30: Adding Variables
Why are we doing this?
We could use PROJECT_LOC for all linked resources or PROJECT_ROOT as the base for build variables
It is “almost” portable, BUT if you move or copy your project, you have to put it at the same “level” in the file system
Defining a link and build variable for TivaWare location gives us a relative path that does NOT depend on location of the project (much more portable)
Also, if we install a new version of TivaWare, we only need to change these variables – which is much easier than creating new relative links
How to add Path and Build Variables
Project  Properties, expand the Resource category, click on Linked Resources. You will see a tab for Path Variables, click New to add a new path variable
Project  Properties, click on Build category, click on the Variables tab, Click New to add a new build variable
Note:
This method defines the variables as part of the project (finer control)
You can also define variables as part of your workspace (do it once)
Embedded Systems: Tiva TM4C123G Homelab
Notes: You could use the pre-defined variables to link all of your resources and this will create an almost portable project. Since the links in your projects are relative to these locations , if you move or copy your project you will have to put them at the same folder level in the file system . Defining a link and build variable for the TivaWare location will give us a relative path that does not depend on the location of the project . This is more portable . Also when the next version of TivaWare arrives , we only need to change these variables which is easier than creating new relative links .
On the CCS menu bar under project, properties expand the resource category and click on linked resources . You’ll see a tab for path variables , click new and add your new path variable .Again in the properties click on the build a category and then click on the variables tab. Click new, to add a new build variable .
In the lab, we’ll add a path variable and build variable called TIVAWARE_INSTALL that will point to the latest TivaWare release.
Note that you can defined variables to be part of your project , or you can define variables that will be part of your workspace and be a part of all projects within it .

## Slide 31: Build Configurations
Code Composer has two pre-defined BUILD CONFIGURATIONS:
  Debug (symbols, no optimization) – great for LOGICAL debug
  Release (no symbols, optimization) – great for PERFORMANCE
Users can create their own custom build configurations
  Right-click on the project and select Properties
  Then click “Processor Options” or any other category:
Notes: Code Composer has two pre-defined build configurations ; debug and release .
The Debug Configuration is great for, as the name implies , debugging . It includes the symbol tables and no optimization .
The release configuration Is better for performance , but contains no simple tables and the code has been optimized . This can make debugging difficult or impossible .
You can create your own custom build configurations by right-clicking on the project and selecting properties . Then click processor options or any of the other categories that you want to change .

## Slide 32: CCSv5 Licensing and Pricing
Licensing
Wide variety of options (node locked, floating, time based)
All versions (full, DSK, free tools) use the same image
Updates readily available online
Pricing
Includes FREE options noted below
Annual subscription - $99 ($159 for floating license)
Item | Description | Price | Annual
Platinum Eval Tools | Full tools with 90 day limit (all EMU) | FREE | 
Platinum Bundle | XDS100 use (EVM or simulator) | FREE | 
Platinum Node Lock | Full tools tied to a machine | $495/$445 | $99
Platinum Floating | Full tools shared across machines | $795 | $159
MSP430 Code-Limited | MSP430 (16KB code limit) | FREE | 
Notes: There are a wide variety of options for licensing code composer studio . Licenses can be node locked, floating or time based . All versions , whether full , boards specific or free use the same image , they are simply licensed differently . Updates to co composer are readily available online .
The platinum evaluation tools are bundled are available for a free 90 day evaluation period. You can purchase a node locked license for either $445US for the download or $495US for the CD. The annual maintenance fee is $99US. The floating license is $795US with a $159US annual Maintenance fee .
The MSP430 16K code limited license is free .
Remember that code composer is free and fully functional when connected to the TM4C123G launchpad board .

## Slide 33: CCSv5 – For More Information
http://processors.wiki.ti.com/index.php/Category:CCS_Training
Notes: For additional training on code composer studio look to the menu bar for tutorials and the Wiki page shown for more detailed training . In this workshop we will barely scratch the surface of code composer’s abilities .

## Slide 34: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter five is an introduction to LM flash programmer

## Slide 35: Introduction to LM Flash Programmer
LM Flash Programmer
Standalone programming GUI that allows to program the flash of a
Tiva C Series device through multiple ports.
Creating the files required for this is a separate build step in Code
Composer.
Install the LM Flash Programmer onto your PC.
Make sure that Code Composer Studio is not actively running code in the CCS
Debug perspective… otherwise CCS and the Flash Programmer may conflict
for control of the USB port.
For More Information
See Programming Example

## Slide 36: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter two is an introduction to TiwaWare

## Slide 37
Peripheral Driver Library
High-level API interface to complete peripheral set
License & royalty free use for TI Cortex-M parts
Available as object library and as source code
Programmed into the on-chip ROM
TivaWare™ for C Series Features
Graphics Library
Graphics primitive and widgets
153 fonts plus Asian and Cyrillic
Graphics utility tools
USB Stacks and Examples
USB Device and Embedded Host compliant
Device, Host, OTG and Windows-side examples
Free VID/PID sharing program
Ethernet
lwip and uip stacks with 1588 PTP modifications
Extensive examples
Extras
Wireless protocols
IQ math examples
Bootloaders
Windows side applications
Sensor Library
An interrupt driven I2C master driver for handling I2C transfers
A set of drivers for I2C connected sensors
A set of routines for common sensor operations
Three layers: Transport, Sensor and Processing
Notes: 37
37
37
TivaWare for C Series is a license and royalty-free set of code for TI Cortex M devices. It includes the peripheral driver library, USB stacks, Ethernet stacks, Graphics library, Sensor library , extensive examples and some additional features. The libraries are available as object and source code. The peripheral driver library is a high-level, API interface to the complete peripheral set. The source code also demonstrates good programming practices should you need to program registers directly. The peripheral driver library is programmed into the on chip ROM of all Tiva C Series devices. Tiva C Series devices are USB device and embedded host compliant. Device, host, on-the-go, and Windows side examples are available. TI has a free vendor ID-product ID sharing program should you wish to use it. Ethernet is supported with lightweight IP and micro IP open source stacks. Both stacks have been modified to support the IEEE-1588 precision time protocol.
The graphics library includes primitives for drawing shapes, text and images on the screen and widgets to tie touch-screen buttons to in-program actions. The library has153 fonts plus Asian and Cyrillic support . Also included are graphics utility tools for converting files and making customized button graphics. The sensor library includes drivers for I2C and the sensors that you’ll find on the SensorHub boosterpack. Examples and a set of common routines for sensor operation are also included. In the extras category we have the simplicity wireless protocol, IQ math examples, boot loaders, and additional Windows side examples.

## Slide 38
In System Programming Options
Tiva Serial Flash Loader
Small piece of code that allows programming of the flash without the need for a debugger interface.
All Tiva C Series MCUs ship with the loader in flash
UART or SSI interface option
The LM Flash Programmer interfaces with the serial flash loader
See application note SPMA029
Tiva Boot Loader
Preloaded in ROM or can be programmed at the beginning of flash to act as an application loader
Can also be used as an update mechanism for an application running on a Tiva microcontroller.
Interface via UART (default), I2C, SSI, Ethernet, USB (DFU H/D)
Included in the Tiva Peripheral Driver Library with full applications examples
Notes: 38
38
38
There are two in-system programming options for you provided through TivaWare. The Tiva serial flash loader is a short piece of code that allows programming of the flash without the need for a debugger like Code Composer Studio. All Tiva C Series microcontrollers ship with this code preloaded in the flash. The loader uses the UART or SSI for communication. It’s meant to be a production-level, low-cost method of programming the part. The LM flash programmer can interface with this loader. The boot loader is preloaded in ROM, or it can be programmed at the beginning of flash to act as an application loader. You can also use it as an update mechanism for an application running on a Tiva microcontroller. This technique is called paging.
The boot loader can boot through the UART, SSI, I2C, CAN, Ethernet, or USB ports. Since full source code is provided, the boot loader can
be completely customized.

## Slide 39: Agenda
Embedded Systems: Tiva TM4C123G Homelab
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Chapter seven is an introduction to homelab workplan

## Slide 40: Homelab Workplan
Base Homelab
  Analyze and experiment workbook tutorial lessons: from Lab1 to Lab9, Lab12 and Lab13 (Lab 10/11/14/15 infeasible without extra HW).
  Write a very small report on the activities, possible encountered problems and significantly results (max 6 slide without Title).
Further works
  Possible final project for embedded system exam
  Integration with others exams and course (ask to
  Prof. Pomante)

## Slide 41: Agenda
Embedded Systems: Tiva TM4C123G Homelab
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Notes: Others case study

## Slide 42: Programming Example
List of proposed Example (presented by Walter Tiberti):
Example 1 : RGB Led and GPIO pins
Example 2 : Timers & Interrupts
Example 3 : ADC
Example 4 : UART
For this example you need to know:
Clock
General Purpose IO
Interrupt
Timer
ADC
UART

## Slide 43: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 44: Fundamental Clock Sources
Precision Internal Oscillator (PIOSC)
  16 MHz ± 3%
Main Oscillator (MOSC) using…
  An external single-ended clock source
  An external crystal
Internal 30 kHz Oscillator
  30 kHz ± 50%
  Intended for use during Deep-Sleep power-saving modes
Hibernation Module Clock Source
  32,768Hz crystal
  Intended to provide the system with a real-time clock source
Notes: There are four fundamental clock sources on Tiva C Series devices which offer the developer very flexible choices when clocking the device. The precision internal oscillator is a 16-megahertz oscillator, plus or minus three percent. No external oscillator or crystal is required.
The main oscillator uses an external, single-ended clock source, or an external crystal. The precision is limited by that of the external source. The internal 30kHz oscillator has an accuracy of plus or minus 50 percent. This oscillator is intended for use during deep sleep, power-saving modes when the actual clock speed is irrelevant to the function of the code. Last is the hibernation module clock source, which requires an external clock crystal. The clock provides the system with a real-time clock source.

## Slide 45: System (CPU) Clock Sources
The CPU can be driven by any of the fundamental clocks …
Internal 16 MHz
Main
Internal 30 kHz
External Real-Time
- Plus -
The internal PLL (400 MHz)
The internal 16MHz oscillator divided by four (4MHz ± 3%)
Clock Source | Drive PLL? | Used as SysClk?
Internal 16MHz | Yes | Yes
Internal 16Mhz/4 | No | Yes
Main Oscillator | Yes | Yes
Internal 30 kHz | No | Yes
Hibernation Module | No | Yes
PLL | - | Yes
Notes: The system clock, or the CPU clock, can be driven by any of the fundamental clocks. The internal 16MHz main oscillator, the internal 30kHz oscillator, and the external real-time oscillator. In addition, we have an internal phase lock loop or PLL that runs at 400 megahertz. No, you can't run the CPU at 400 megahertz. Dividers limit you to 80 megahertz and below. We also have a divider on the internal 16-megahertz oscillator, that provides four megahertz plus or minus three percent.
You have six different clock sources that can drive the CPU.
Only the internal 16MHz and Main oscillators can drive the PLL.

## Slide 46: Tiva C Series Clock Tree
driverLib API SysCtlClockSet() selects:
SYSDIV divider setting
OSC or PLL
Main or Internal oscillator
Crystal frequency
Notes: This is the Tiva C Series clock tree. Its flexible implementation provides you with the different types of clocks that you need for low-power operation, for low-cost operation and for high-precision operation. On the previous slide we looked at the possible sources for the System Clock. If you find the System Clock line on the right of this diagram and follow it back through the multiplexors you’ll find that any of the four fundamental clock sources can drive the System Clock.
As an example, let’s connect a 16MHz crystal to the inputs of the main oscillator there on the left. You should bear in mind that there are restrictions on the crystal frequency. Working our way to the right, let’s also use the PLL and divide it properly to drive the System Clock at 80MHz or below.
Making all those selections is simplified with the use of the TiveWare API shown at the bottom of the slide. A single line of code can make all of the choices shown to program the System Clock selections.

## Slide 47: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 48: General Purpose IO
  Any GPIO can be an interrupt:
    Edge-triggered on rising, falling or both
    Level-sensitive on high or low values
  Can directly initiate an ADC sample sequence or µDMA transfer
  Toggle rate up to the CPU clock speed on the Advanced High-Performance Bus. ½ CPU clock speed on the Standard.
  5V tolerant in input configuration
  Programmable Drive Strength (2, 4, 8mA or 8mA with slew rate control)
  Programmable weak pull-up, pull-down, and open drain
  Pin state can be retained during Hibernation mode
Notes: Tiva C Series general-purpose IO is extremely flexible. Any GPIO can be an interrupt; edge-triggered on rising, falling, or both. It can be level-sensitive to high or low values. Any GPIO can directly initiate an ADC sample sequence or a DMA transfer. The toggle rate can be as high as the CPU clock speed on the advanced high-performance bus. As inputs, all of the GPIO are 5V tolerant.
As outputs, the drive strength is programmable to be 2, 4 or 8mA. The 8mA setting also allows you to configure the slew rate.
The GPIO pins have programmable weak pull-up, pull-down, and open-drain modes.
The pin states can be retained during hibernation mode to correctly connect to external circuitry even while the device sleeps.

## Slide 49: GPIO Address Masking
0
0
1
0
0
1
1
0
0
0
0
0
0
…
The register we want to change is GPIO Port D (0x4005.8000) Current contents of the register is:
0
0
0
1
1
1
0
1
Instead of writing to GPIO Port D directly, write to 0x4005.8098. Bits 9:2 (shown here) become a bit-mask for the value you write.
0
0
1
1
1
0
1
1
1
1
1
0
1
0
1
1
Only the bits marked as “1” in the bit-mask are changed.
GPIO Port D (0x4005.8000)
The value we will write is 0xEB:
Write Value (0xEB)
New value in GPIO Port D (note that only the red bits were written)
Each GPIO port has a base address. You can write an 8-bit value directly to this base address and all eight pins are modified. If you want to modify specific bits, you can use a bit-mask to indicate which bits are to be modified. This is done in hardware by mapping each GPIO port to 256 addresses. Bits 9:2 of the address bus are used as the bit mask.
GPIOPinWrite(GPIO_PORTD_BASE, GPIO_PIN_5|GPIO_PIN_2|GPIO_PIN_1, 0xEB);
Note: you specify base address, bit mask, and value to write. The GIPOPinWrite() function determines the correct address for the mask.
Notes: GPIO address masking is a somewhat unusual technique for programming the GPIO port pins. Each GPIO port has a base address, and if you look in the diagram, GPIO port D has a base address of 40058000. You can write an 8-bit value to the port directly to that base address, and all eight pins will be modified, just like has been done to GPIO ports since the earliest microcontrollers.
If you want to modify specific bits of that port, you would have to read the value on the port pins, change the specific bits, and then write the value back out to the port. This is a read-modify-write operation fraught with issues. For instance, if an interrupt changed a pin state during this process, your code would write the wrong value to the pin.
On the Tiva C Series parts, each port has 256 possible addresses covering every possible combination of the port pins. The GPIOPinWrite() API uses the pin-mash and the base address to form the address that allows us to write to the specified pins. In this case, pins 1, 2 and 5. We can then write or read from those pins only. You should appreciate that this is not a software masking trick, this technique is completely in the hardware.

## Slide 50: Critical Function GPIO Protection
Six pins on the device are protected against accidental programming:
  PC3,2,1 & 0: JTAG/SWD
  PD7 & PF0: NMI
Any write to the following registers for these pins will not be stored unless the GPIOLOCK register has been unlocked:
  GPIO Alternate Function Select register
  GPIO Pull Up or Pull Down select registers
  GPIO Digital Enable register
The following sequence will unlock the GPIOLOCK register for PF0 using direct register programming:
HWREG(GPIO_PORTF_BASE + GPIO_O_LOCK) = GPIO_LOCK_KEY;
HWREG(GPIO_PORTF_BASE + GPIO_O_CR) |= 0x01;
HWREG(GPIO_PORTF_BASE + GPIO_O_LOCK) = 0;
Reading the GPIOLOCK register returns it to lock status
Notes: Six of the pins on the TM4C123GH6PM have critical functions that are protected from accidental disruption. These are the four emulation pins and the two pins dedicated to the non maskable interrupt.
Any write to the alternate function select, pull-up, pull-down or digital enable registers for these pins will not be stored unless the GPIOLOCK register has been unlocked.
The coding sequence shown uses direct register writes to unlock the GPIOLOCK feature of Port F pin 0. Any read of the GPIOLOCK register will return it to locked status.

## Slide 51: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 52: Nested Vectored Interrupt Controller (NVIC)
Handles exceptions and interrupts
8 programmable priority levels, priority grouping
7 exceptions and 71 Interrupts
Automatic state saving and restoring
Automatic reading of the vector table entry
Pre-emptive/Nested Interrupts
Tail-chaining
  Deterministic: always 12 cycles or 6 with tail-chaining
t
Motor control ISRs (e.g. PWM, ADC)
Communication ISRs (e.g. CAN)
Main application (foreground)
Notes: The Tiva C Series Nested Vectored Interrupt Controller, or NVIC, is tightly coupled to the central processing unit. It handles all of the exceptions and interrupts that come into the CPU. There are eight programmable priority levels and priority grouping. In most microcontroller interrupt vector tables, the priority levels for each peripheral are set by the manufacturer, and you have no input into what they are. That's not the case on this device. You can reprogram the priorities as you like.
This device has 7 system level exceptions and 65 peripheral interrupts. It has automatic state save and restore for entering and exiting Interrupt Service Routines, as well as automatic reading of the vector table entry to quickly facilitate this process.
One of the first rules that you learn when programming interrupts on a microcontroller is to not nest interrupts, but sometimes you need to nest the interrupts. For instance, you need to get to a very low latency motor control or device. You need to get to it very quickly, and you have other interrupts that take too long. Those long ISRs will need to be interruptible. On most microcontrollers you will have to program this tedious process in software.
On the Tiva C Series devices, you can do it by programming the NVIC hardware. You can make interrupts preemptive, and you can nest them. Interrupts can also be tail-chained, which is something I'll explain in the next few slides. Interrupts are deterministic. They're always either 12 cycles or 6 cycles if they're tail-chained.
Taking a look at the diagram at the bottom, we can see this is an application with a two interrupts. From left to the right, the first interrupt that goes off is for motor control. Motor control requires extremely low latency. You can't wait. You must act on the interrupt quickly.
The second interrupt is a repeat of the first.
In the third instance, a communication interrupt like the CAN has started operation. Communication interrupts using involve FIFO’s and buffers, so they can wait. When the motor control interrupt arrives, we can't wait for the communications ISR to complete, the motor control ISR must preempt it.
The remaining instances are further examples. Remember that the nesting behavior is programmed into the NVIC hardware.

## Slide 53: Cortex-M4® Interrupt Handling
Interrupt handling is automatic. No instruction overhead.
Entry
  Automatically pushes registers R0–R3, R12, LR, PSR, and PC onto the stack
  In parallel, ISR is pre-fetched on the instruction bus. ISR ready to start executing as soon as stack PUSH complete
Exit
  Processor state is automatically restored from the stack
  In parallel, interrupted instruction is pre-fetched ready for execution upon completion of stack POP
Notes: Cortex M4 interrupt handling is totally automatic, s there's no instruction overhead. On entry the device automatically pushes registers R0 through R3, R2, the LR, the PSR, and the program counter onto the stack. In parallel, the address of the applicable interrupt service routine is pre-fetched onto the instruction bus. The ISR is then ready to start executing as soon as the last stack push is complete.
On the exit side, the processor state is automatically restored from the stack. In parallel, the address of the interrupted instruction is pre-fetched, ready for execution upon completion of the final stack pop.

## Slide 54: Cortex-M4® Exception Types
Vector Number | Exception Type | Priority | Vector address | Descriptions
1 | Reset | -3 | 0x04 | Reset
2 | NMI | -2 | 0x08 | Non-Maskable Interrupt
3 | Hard Fault | -1 | 0x0C | Error during exception processing
4 | Memory Management Fault | Programmable | 0x10 | MPU violation
5 | Bus Fault | Programmable | 0x14 | Bus error (Prefetch or data abort)
6 | Usage Fault | Programmable | 0x18 | Exceptions due to program errors
7-10 | Reserved | - | 0x1C - 0x28 | 
11 | SVCall | Programmable | 0x2C | SVC instruction
12 | Debug Monitor | Programmable | 0x30 | Exception for debug
13 | Reserved | - | 0x34 | 
14 | PendSV | Programmable | 0x38 | 
15 | SysTick | Programmable | 0x3C | System Tick Timer
16 and above | Interrupts | Programmable | 0x40 | External interrupts (Peripherals)
Notes: Exception types on the Cortex M4 include reset, the non-maskable interrupt, hard fault and the 7 shown in the table. Note the priority levels for the rest, NMI and hard faults. Only those cannot be changed.
A HardFault is all classes of fault, when the corresponding fault handler cannot be activated because it is currently disabled or masked by exception masking
A Memory management fault is caused by a Memory Protection Unit violation or invalid accesses (such as an instruction fetch from a non-executable region)
Bus faults are an Error response received from the bus system; caused by an instruction prefetch abort or data access error
Usage faults are caused by invalid instructions or invalid state transition attempts
SVCall is a System service call via SVC instruction
Not that the priority is programmable for most of these faults.

## Slide 55: Cortex-M4® Vector Table
After reset, vector table is located at address 0
Each entry contains the address of the function to be executed
The value in address 0x00 is used as starting address of the Main Stack Pointer (MSP)
Vector table can be relocated by writing to the VTABLE register (must be aligned on a 1KB boundary)
Open startup_ccs.c to see vector table coding
Notes: After reset, Cortex M4 vector table is located at address zero. Each entry in the vector table contains the address of the handler or ISR to be executed.
If you look down at the bottom at the initial SP value, that value at address 00 is used as a starting address of the main stack pointer.
It’s typical to relocate the vector table after bootloading the device and this can be done by writing to the VTABLE register. The vector table must be aligned on a 1K byte boundary. If you like, open up startup_ccs.c in Code Composer for a complete view of the vector table.

## Slide 56: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 57: General Purpose Timer Module
Six 16/32-bit and Six 32/64-bit general purpose timers
Twelve 16/32-bit and Twelve 32/64-bit capture/compare/PWM pins
Timer modes:
  One-shot
  Periodic
  Input edge count or time capture with 16-bit prescaler
  PWM generation (separated only)
  Real-Time Clock (concatenated only)
Count up or down
Simple PWM (no deadband generation)
Support for timer synchronization, daisy-chains, and stalling during debugging
May trigger ADC samples or DMA transfers
Notes: The General Purpose Timer Module, or GPTM, has six 16 or 32-bit and six 32 or 64-bit general-purpose timers. They can be used for capture, compare, or PWM. There are 5 different time modes available: one shot, periodic, input edge count or time capture, PWM generation and Real time clock.
The timers can count up or down.
PWM generation is simple with no deadband generation and software inversion of the outputs.
The module supports synchronization across multiple timers, daisy chaining and user enabled stalling during debugging. This last feature stalls the timers during debug when the user clicks the halt button and prevents unwanted timer interrupts from occurring.
The timers can also trigger the ADC sample sequencer or DMA transfers.

## Slide 58: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 59: Analog-to-Digital Converter
Tiva TM4C MCUs feature two ADC modules (ADC0 and ADC1) that can be used to convert continuous analog voltages to discrete digital values
Each ADC module has 12-bit resolution
Each ADC module operates independently and can:
  Execute different sample sequences
  Sample any of the shared analog input channels
  Generate interrupts & triggers
ADC
VIN
VOUT
Input Channels
Triggers
Interrupts/ Triggers
Interrupts/ Triggers
12
VIN
VOUT
000
001
011
010
100
101
t
t
ADC1
ADC0
Notes: Tiva C Series microcontrollers feature two ADC modules, ADC0 and ADC1, that can be used to convert continuous analog voltages to discrete digital values. Each one of those modules has 12 bits of resolution, can operate independently and can execute different sample sequences. You can sample any of the shared analog input channels, single ended or differential and you can generate interrupts and triggers.

## Slide 60: TM4C123GH6PM ADC Features
Two 12-bit 1MSPS ADCs
12 shared analog input channels
Single ended & differential input configurations
On-chip temperature sensor
Maximum sample rate of one million samples/second (1MSPS).
Fixed references (VDDA/GNDA) due to pin-count limitations
4 programmable sample conversion sequencers per ADC
Separate analog power & ground pins
Flexible trigger control
  Controller/ software
  Timers
  Analog comparators
  GPIO
2x to 64x hardware averaging
8 Digital comparators / per ADC
2 Analog comparators
Optional phase shift in sample time, between ADC modules … programmable from 22.5 ° to 337.5°
ADC
VIN
VOUT
Notes: Due to the low pin count of the LaunchPad device, there is a fixed reference between the analog voltage and ground and 12 shared I/O.
There are four programmable sample conversion sequencers per ADC that we'll deal with on the next slide. Separate analog power and ground pins keep the noise between the digital and analog sides low.
There are 5 ways to trigger a measurement … with software, when a timer expires, on an analog comparison event or using a GPIO pin.
Hardware averaging can take 2, 4, 8, 16, 32 or 64 samples and average them together to generate each result..
Each ADC has eight digital comparators for a total of 16. There are two analog comparators for the device. Optionally, you can phase shift the sample time between the ADC modules, between 22.5 to 337.5 degrees.

## Slide 61: ADC Sample Sequencers
Tiva TM4C ADC’s collect and sample data using programmable sequencers.
Each sample sequence is a fully programmable series of consecutive (back-to-back) samples that allows the ADC module to collect data from multiple input sources without having to be re-configured.
Each ADC module has 4 sample sequencers that control sampling and data capture.
All sample sequencers are identical except for the number of samples they can capture and the depth of their FIFO.
To configure a sample sequencer, the following information is required:
  Input source for each sample
  Mode (single-ended, or differential) for each sample
  Interrupt generation on sample completion for each sample
  Indicator for the last sample in the sequence
Each sample sequencer can transfer data independently through a dedicated μDMA channel.
Sequencer | Number of Samples | Depth of FIFO
SS 3 | 1 | 1
SS 2 | 4 | 4
SS 1 | 4 | 4
SS 0 | 8 | 8
Notes: The analog to digital converters collect and sample their data using programmable sequencers. Each sample sequence is a fully programmable series of consecutive samples that allows the ADC to collect data from multiple input sources without having to be reconfigured. Each one of the modules has four sample sequencers that control the sampling and data capture. They are identical except for the number of samples that they can capture and the depth of the associated FIFO.
In order to configure a sample sequence, the following information is required for each sample: the input source, whether the mode is single ended or differential, whether or not to generate an interrupt and whether this is the final sample in the sequence.
Each sample sequencer can then transfer its data from the FIFO independently using a dedicated DMA channel.

## Slide 62: Agenda
Introduction (ARM® Cortex™-M4F, Memory and Peripherals)
Development Tools
Hardware and Software Setup
Code Composer Studio
LM Flash Programmer
Introduction to TivaWare™
HomeLab Workplan
Programming Example
Clock
General Purpose IO
Interrupt
Timer
ADC
UART
Embedded Systems: Tiva TM4C123G Homelab
Notes: Others case study

## Slide 63: UART Features
Separate 16x8 bit transmit and receive FIFOs
Programmable baud rate generator
Auto generation and stripping of start, stop, and parity bits
Line break generation and detection
Programmable serial interface
  5, 6, 7, or 8 data bits
  even, odd, stick, or no parity bits
  1 or 2 stop bits
  baud rate generation, from DC to processor clock/16
Modem flow control on UART1 (RTS/CTS)
IrDA and EIA-495 9-bit protocols
µDMA support
Notes: The TM4C123GH6PM includes 8 UART ports. Each of these ports features:
Separate 16 x 8-bit transmit and receive FIFOs
A programmable baud rate generator
Automatic generation and removal of the start, stop and parity bits
Line break generation and detection
A choice of 5 to 8 data bits, multiple parity types and 1 or 2 stop bits
Modem and flow control
IrDA and EIA-495 9-bit protocols
DMA support with separate transmit and receive channels

## Slide 64: Block Diagram
Notes: Note the two external pins on the right. Tiva C Series pins are highly multiplexed with other functions. Also note the transmit and receive FIFOs are integral to the module itself.

## Slide 65: Basic Operation
Initialize the UART
  Enable the UART peripheral, e.g.
    SysCtlPeripheralEnable(SYSCTL_PERIPH_UART0);
    SysCtlPeripheralEnable(SYSCTL_PERIPH_GPIOA);
  Set the Rx/Tx pins as UART pins
    GPIOPinConfigure(GPIO_PA0_U0RX);
    GPIOPinConfigure(GPIO_PA1_U0TX);
    GPIOPinTypeUART(GPIO_PORTA_BASE, GPIO_PIN_0 | GPIO_PIN_1);
  Configure the UART baud rate, data configuration
    ROM_UARTConfigSetExpClk(UART0_BASE, ROM_SysCtlClockGet(), 115200,
    UART_CONFIG_WLEN_8 | UART_CONFIG_STOP_ONE |
    UART_CONFIG_PAR_NONE));
  Configure other UART features (e.g. interrupts, FIFO)
Send/receive a character
  Single register used for transmit/receive
  Blocking/non-blocking functions in driverlib:
    UARTCharPut(UART0_BASE, ‘a’);
    newchar = UARTCharGet(UART0_BASE);
    UARTCharPutNonBlocking(UART0_BASE, ‘a’);
    newchar = UARTCharGetNonBlocking(UART0_BASE);
Notes: The basic steps for initializing the UART are as follows:
Enable the UART peripheral
Configure the transmit and receive pins for the UART function
Configure the baud rate and data set up of the UART
Configure any other UART features like interrupt generation and FIFO usage
Now the port is ready to send and receive characters. In this UART design, a single data register is used for both the transmit and receive function. The peripheral driver library supports both blocking and non blocking APIs for writing and reading the data register.

## Slide 66: UART Interrupts
Single interrupt per module, cleared automatically
Interrupt conditions:
  Overrun error
  Break error
  Parity error
  Framing error
  Receive timeout – when FIFO is not empty and no further data is received over a 32-bit period
  Transmit – generated when no data present (if FIFO enabled, see next slide)
  Receive – generated when character is received (if FIFO enabled, see next slide)
Interrupts on these conditions can be enabled individually
Your handler code must check to determine the source of the UART interrupt and clear the flag(s)
Notes: Each UART module can provide an interrupt to the CPU. Since this is a single source interrupt, it will be cleared automatically . Conditions under which an interrupt can be generated are:
An overrun error
A break error
An incorrect parity
A framing error
A receive timeout when the fifo is not empty and no data is received during 32 bit times
When a transmit is attempted and no data is present to be transmitted
When a character is received
Interrupts on all these conditions can be enabled individually. Since these conditions are OR’d into a single interrupt to the CPU , the handler code must check to determine which of these conditions triggered the interrupt and clear the appropriate flags .

## Slide 67: Using the UART FIFOs
Both FIFOs are accessed via the UART Data register (UARTDR)
After reset, the FIFOs are enabled*, you can disable by resetting the FEN bit in UARTLCRH, e.g.
UARTFIFODisable(UART0_BASE);
Trigger points for FIFO interrupts can be set at 1/8, 1/4, 1/2,3/4, 7/8 full, e.g.
UARTFIFOLevelSet(UART0_BASE,
UART_FIFO_TX4_8,
UART_FIFO_RX4_8);
Transmit FIFO
UART_FIFO_TX4_8
UART_FIFO_TX1_8
UART_FIFO_TX2_8
UART_FIFO_TX6_8
UART_FIFO_TX7_8
FIFO Level Select
* Note: the datasheet says FIFOs are disabled at reset
Notes: Both the transmit and receive fifo’s are accessed through the UART Data register .
While the datasheet indicates that the UART fifo’s are disabled at reset, basic configuration of the UART module re-enables this feature by default. They can easily be disabled if necessary.
Trigger points for the generation of UART interrupt can be set at the 1/8th, 1/4th, ½, ¾, 7/8 and full points.

## Slide 68: UART “stdio” Functions
TivaWare “utils” folder contains functions for C stdio console functions:
  c:\TivaWare\utils\uartstdio.h
  c:\TivaWare\utils\uartstdio.c
Usage example:
  UARTStdioInit(0); //use UART0, 115200
  UARTprintf(“Enter text: “);
See uartstdio.h for other functions
Notes:
  Use the provided interrupt handler UARTStdioIntHandler() code in uartstdio.c
  Buffering is provided if you define UART_BUFFERED symbol
    Receive buffer is 128 bytes
    Transmit buffer is 1024 bytes
Notes: TivaWare’s UART library includes standard I/O console functions for initialization, printf, get, flushing the FIFOs and others.
To use the functions you should use the interrupt handler provided in uartstdio.c

## Slide 69: Other UART Features
Modem flow control on UART1 (RTS/CTS)
IrDA serial IR (SIR) encoder/decoder
  External infrared transceiver required
  Supports half-duplex serial SIR interface
  Minimum of 10-ms delay required between transmit/receive, provided by software
ISA 7816 smartcard support
  UnTX signal used as a bit clock
  UnRx signal is half-duplex communication line
  GPIO pin used for smartcard reset, other signals provided by your system design
LIN (Local Interconnect Network) support: master or slave
µDMA support
  Single or burst transfers support
  UART interrupt handler handles DMA completion interrupt
EIA-495 9-bit operation
  Multi-drop configuration: one master, multiple slaves
  Provides “address” bit (in place of parity bit)
  Slaves only respond to their address
Notes: UART1 supports modem flow control with Request to Send and Clear to Send handshake signals.
Infrared, ISA7816 smartcard, Local Interconnect Network and EIA-495 support is part of all UART modules.
UART modules have separate transmit and receive channels for efficient transfers of data.

## Slide 70: Thanks for Attending!

## Slide 71
Presented by
Vittoriano Muttillo
PhD Student