## Slide 1: Introduction to VHDL
Embedded Systems
Università degli Studi dell’Aquila
Notes: Ricordare di mandare email a Pomante con nome ed email.
Rivedere dove si è arrivati con il corso.
MODELLO:
Hanno trattato le tecnologie full-custom, standard cell, etc.
Fare esempio di circuito full custom (memoria nand flash)
Uno dei vantaggi delle standard cells: il tempo di test.
Problema delle standard cells: se abbiamo strutture fisse, realizzare grandi e complicati progetti è difficile. Questo limite è risolto, per esempio, dalle FPGA.
Con le FPGA è richiesto:
- Need to model at higher abstraction level the desired functionality
- A sw tool that allows to design and validate and configure FPGA.
Se risolviamo i 2 punti, potremo dire che con le FPGA si abbassa la NRE.
Oggi le FPGA hanno bassi costi, unitamente alle loro schede di sviluppo, quindi che ce le possiamo comprare anche noi!
Farò vedere, nella prossima lezione, come si programma una FPGA.

## Slide 2: Outline
Hardware Description Languages
Concurrent and sequential area of VHDL
Simulation
GCD Calculator
Testbench
FPGA Design Tools
References

## Slide 3: Hardware description languages
An HDL (Hardware Description Language) is a language for the description of digital electronic circuits
Hardware functionalities are described independently from the implementation
How many types of implementation do you know?
  Recall the Hardware Technologies chapter
Notes: Cosa mi serve per poter usare una FPGA? Mi serve poter descrivere il mio algoritmo in una maniera astratta, che si astragga, appunto, dalla parte di interconnessioni a basso livello.
Mi serve poi un algoritmo che mi passi dalla descrizione astratta, ad una implementazione su chip: quindi mi serve un software.
Questo breve minicorso focalizzerà su questi due concetti: un metodo di descrizione astratta, per implementare algoritmi su FPGA, e un metodo di implementazione (i software, che faremo nella successiva lezione).

## Slide 4: Key distinctive elements of HDL
With respect to a programming language, HDL languages allow to describe:
  The timing characteristics: within hardware systems, there is the propagation delay of signals.
  The parallelism: blocks that compose a particular system evolve at the same time during a particular time interval.
S1
S2
y1
y2
x
t

## Slide 5: Domains and abstraction levels
A digital circuit can be described at:
  Physical level: physical devices that compose the system are considered.
  Structural level: system is described by means of simpler sub-blocks that compose the system itself.
  Behavioural level: it is described only the functionality of the system, i.e., the relation between inputs and outputs.

## Slide 6: Y-chart
Notes: Far notare dove si va a piazzare il dataflow level. Precisamente, il dataflow level può vedersi come un parallelo del livello RT.

## Slide 7: Description goals
A description language is not executable
Digital circuit description has the following goals:
  Simulation: it is checked if the circuit behaviour has the expected trend.
  Synthesis: a final implementation is produced starting from the HDL.
Not all the constructs that can be simulated are synthesizable.
Digital
Circuit Design
Hardware description
Simulation
Synthesis
Notes: Soffermarsi bene su questo
Il VHDL è stato pensato per la simulazione e la descrizione di circuiti hardware, poi si è pensato alla sintesi.

## Slide 8: Main description languages
* Reference: SystemC: from the ground up, Wiley, 2010

## Slide 9: VHDL language
VHDL stands for VHSIC (Very High Speed Integrated Circuits) Hardware Description Language
It has been developed in the early ‘80 years from Defense Department of USA and publicly released in 1985.
Standard IEEE 1076-1987, reviewed in 1993 and 2008

## Slide 10: ADA and VHDL
The VHDL has been developed starting from ADA programming language, inheriting a lot of elements:
  Conceptually: highly typed language, not case sensitive;
  Syntactically, for example:
  -- This is a VHDL comment

## Slide 11: Verilog language
Verilog Hardware Description Language, usually called Verilog
It has been developed in the early 1984 by Phil Moorby at Gateway Design Automation.
Verilog-XL simulator sold by Gateway
IEEE standard 1364 in December 1995

## Slide 12: VHDL vs Verilog
 | VHDL | Verilog
Reusability | Packages | -
Easy to understand | Strongly typed | More intuitive
Back annotation | - | Verilog uses the Standard Delay Format (SDF)
High level constructs | Many available constructs | -
Large designs | Package and Generate | verbose descriptions
Readability | Similar to ADA | Similar to C
Structural replication | Generate | -

## Slide 13: Design units
Design Units are VHDL code segments that can be separately processed and included in a library.
A VHDL description of a digital system must contain at least one entity and one architecture.
  An entity specifies univocally the identifying name of a system and the characteristics of its inputs and outputs.
  In the architecture, instead, the circuit functionality is described.

## Slide 14: A simple example: half adder
Half adder:
  Receives 2 bits as input (A,B);
  Generates an output bit equal to the sum of 2 input bits (SUM);
  Generates an output bit equal to carry (CARRY);
Half Adder
A
B
SUM
CARRY

## Slide 15: Half adder: functional specifications
From functional description it is possible to fill the truth table and obtain the circuit structure
A | B | SUM | CARRY
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 16: Half adder: entity
The following VHDL entity corresponds to the top level of the circuit:
-- Entity declaration of half adder
entity half_adder is
port
(
  A: in bit;
  B: in bit;
  SUM: out bit;
  CARRY: out bit
);
end half_adder ;

## Slide 17: Half adder: architecture (1)
The functionality is described in the architecture associated to the entity
architecture ha_arch of half_adder is
begin
end ha_arch ;
Instructions contained in concurrent area are treated as parallelly evolving
Concurrent area

## Slide 18: Concurrent area: constructs (1)
Concurrent assignment:
  The <= operator is used to assign values to a signal
Z <= A;
Z <= '1';
Z_vector <= "10001";
Conditional assignment:
  When a certain condition is verified, a value is assigned to a signal
  Z <= A when SEL = "00" else
  B when SEL = "11" else
  C;

## Slide 19: Concurrent area: constructs (2)
Assignment with selection:
  Similar to the conditional assignment, it allows to quickly enumerate a lot of different cases
  Similar to if and switch-case instructions of C language
  with SEL select
  Z <= A when "000",
  B when "001",
  C when "010",
  D when "011"
  E when others ;

## Slide 20: Half adder: architecture (2)
Boolean operators are used to describe computations, while the assignment operator is used to describe the functionality
architecture ha_arch of half_adder is
begin
SUM <= A xor B;
CARRY <= A and B;
end ha_arch ;
Each architecture makes reference at only one entity, but multiple architectures can refer to the same entity (set by means of an opportune configuration file, not detailed here).

## Slide 21: Description styles and abstraction levels
VHDL language allows the description of the circuit behaviour following three different styles:
  Behavioural: the circuit functionality in algorithmic terms is described, or it is specified how data move internally to the system;
  Structural: the system is described as interconnection of base components;
  Dataflow: the flow of data internally to the system is described, using concurrent assignments;
Different types of descriptions can be combined with respect of necessity.

## Slide 22: Example: full adder
A full adder is a digital circuit with three inputs and two outputs.
The sum of the two input bits is calculated, and it is able to account for a carry coming from previous sum
Full Adder
A
B
S
Cout
Cin
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 23: Full adder: entity
A full adder entity:
entity FULL_ADDER is
port (A, B, Cin : in bit ;
S , Cout : out bit );
end FULL_ADDER ;

## Slide 24: Full adder: entity
A full adder entity:
entity FULL_ADDER is
port (A, B, Cin : in bit ;
S , Cout : out bit );
end FULL_ADDER ;
BAD DESCRIPTION STYLE !

## Slide 25: Full adder: entity
A full adder entity:
entity FULL_ADDER is
port (A : in bit;
B : in bit;
Cin : in bit ;
S : out bit;
Cout : out bit
);
end FULL_ADDER ;
GOOD DESCRIPTION STYLE !

## Slide 26: Full Adder: architecture
  architecture Behavioural of full_adder is
  begin
  end Behavioural;
Concurrent Area

## Slide 27: Full Adder architecture (Behavioural)
The behavioural level is the highest level description available in VHDL language.
The base construct is the process: a process allows to open a "sequential execution area" internally to a concurrent area.
  architecture Behavioural of full_adder is
  begin
  sum : process (A,B,Cin)
  begin
  end Behavioural;
Sequential Area
Concurrent Area

## Slide 28: Full Adder architecture (Behavioural)
The behavioural level is the highest level description available in VHDL language.
The base construct is the process: a process allows to open a "sequential execution area" internally to a concurrent area.
  architecture Behavioural of full_adder is
  begin
  sum : process (A,B,Cin)
  begin
  end Behavioural;
Sequential Area
Concurrent Area
Concurrent Area

## Slide 29: Full Adder architecture (Behavioural)
The behavioural level is the highest level description available in VHDL language.
The base construct is the process: a process allows to open a "sequential evolution area" internally to a concurrent area.
Description of the Truth Table of the Full Adder using a Process
  architecture Behavioural of full_adder is
  begin
  sum : process (A,B,Cin)
  begin
  end process;
  end Behavioural;
Concurrent Area
Concurrent Area

## Slide 30: Process
A process can be declared everywhere in the architecture body, because what there is inside it evolves in concurrent manner with other statements in concurrent area.
A process opens a sequential area internally to the concurrent area: statements contained in a process evolve serially.
The evolution happens in correspondence of a specified event in the sensitivity list.

## Slide 31: Sensitivity list
The sensitivity list contains all the signals to which the process must be sensible.
Each time that a signal in the sensitivity list changes value, the process is activated.
  architecture Behavioural of full_adder is
  begin
  sum : process (A,B,Cin)
  begin
  end process;
  end Behavioural;
Sequential Area
Sensitivity List

## Slide 32: Sequential area constructs (1)
Internally to the process, VHDL statements evolve sequentially "as in a classical programming language".
Conditional choice, for example, is available:
if condition then
sequential statements
[ elsif condition then
sequential statements ]
[ else
sequential statements ]
end if;

## Slide 33: Sequential area constructs (2)
Multiple choice: it is the same of switch-case construct:
case expression is
  when choice =>
  sequential statements
  when choice =>
  sequential statements
  [when others =>
  sequential statements]
end case ;
Others constructs are available in sequential area.

## Slide 34: Full Adder architecture (Behavioural) (1)
architecture Behavioural of full_adder is
begin
process(A,B,Cin)
begin
if(A='0' and B='0' and Cin='0')then
S<='0';
Cout<='0';
elsif( A='0' and B='0' and C='1')then
S<='1';
Cout<='0';
elsif( A='0' and B='1' and C='0')then
S<='1';
Cout<='0';
elsif( A='0' and B='1' and C='1')then
S<='0';
Cout<='1';

## Slide 35: Full Adder architecture (Behavioural) (2)
elsif( A='1' and B='0' and C='0')then
S<='1';
Cout<='0';
elsif( A='1' and B='0' and C='1')then
S<='0';
Cout<='1';
elsif( A='1' and B='1' and C='0')then
S<='0';
Cout<='1';
else
S<='1';
Cout<='1';
end if;
end process;
end Behavioural ;

## Slide 36: Full Adder description
We can synthesize the Full Adder with a "direct synthesis", obtaining a logic gates network.
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 37: Full Adder architecture (Dataflow)
The propagation of flow of data internally to the circuit is described
For example in the Full-Adder:
architecture dataflow of full_adder is
S <= A xor B xor C_in ;
Cout <= (A and B) or (C_in and (A or B));
end dataflow ;

## Slide 38: Full Adder as multiple Half Adders
It can be noted, from the Truth Table, that the Full Adder functionality can be obtained by appropriately combining two Half-Adders.
Half adder
Half adder

## Slide 39: Signals and Components
The architecture describes the functionality of the instantiated circuit.
Over the architecture body itself it is present also a declarative area in which is possible to declare signals and components:
architecture name of entity_name is
component INV
port ( ... );
end component ;
signal s1,c1,c2 : bit;
begin
Declaration
Area
Signals are not visible out of the module itself.

## Slide 40: Structural view
By using components it is possible to model system as interconnection of previous defined subsystems:
  The port map construct allows to instantiate the components and to define the interconnections.
  The signals are used to represent connections among components.

## Slide 41: Generic construct
VHDL supports the construction of parametric components through the generic construct
entity half_adder is
generic (N: integer);
port (A, B: in std_logic_vector (N-1 downto 0);
In addition to the port map, the instantiation of a parametric component will include also a generic map
generic map (N => 10)

## Slide 42: Full Adder architecture (Structural) (1)
  architecture struct of full_adder is
  signal s1 ,c1 ,c2: bit ;
  component half_adder
  port (A: in bit;
  B: in bit ;
  S: out bit;
  Cout: out bit
  );
  end component ;

## Slide 43: Full Adder architecture (Structural) (2)
  begin
    HA1 : half_adder
    port map( A => a,
    B => b,
    S => s1,
    Cout => c1
    );
    HA2 : half_adder
    port map( A => s1,
    B => Cin,
    S => S,
    Cout => c2
    );
    Cout <= c1 or c2;
  end struct ;

## Slide 44: VHDL Data types
In VHDL, bit and bitvector types are available for digital data representation
It is usually preferred to use std_logic and std_logic_vector defined in the std_logic_1164 library
The library must be always declared in the following manner:
library IEEE ;
use IEEE.std_logic_1164.ALL;

## Slide 45: IEEE std_logic_1164 types
The defined types in std_logic_1164 library use a 9 values logic system:
  '0': zero value;
  '1': one value;
  'Z': high impedance;
  'U': uninitialized;
  'X': undefined;
  '-': don't care;
library IEEE ;
use IEEE.STD_LOGIC_1164.ALL;
...
signal X: std_logic;
signal Y: std_logic_vector (7 downto 0);

## Slide 46: Combinatorial circuits (1)
A combinatorial circuit can be described by a logic expression, combination of Boolean operators and, or, not
  The VHDL makes available these operators
  Y <= not(A) and B;
Alternatively it is possible to use a truth table
  Into VHDL a concurrent conditional assignment is used
  The table can be also not completely specified
with X select
Y <= "01" when "00",
"10" when "11",
"--" when others;

## Slide 47: Combinatorial circuits (2)
A combinatorial circuit can be described also using a process
  Recall the truth table description for the full adder, that is a combinatorial block
  Combinatorial means that outputs are evaluated whenever there is an input variation. Outputs are produced with a delay depending on the circuit complexity.
  From the point of view of hardware description, this means that we need to enter into a VHDL-process every time there is an input variation.
  Recalling that theory of VHDL-processes expects sensitivity lists, we can conclude that, in order to describe a combinatorial circuit with a process, all the inputs must be in the sensitivity list.

## Slide 48: Sequential circuits
They can be synchronous and asynchronous. In digital design it is preferred to use synchronous systems.
In VHDL the description of sequential circuits can be done by means of process statement
  Example: Counter
  -- Commutation on clock rising edge:
  counter : process(CLOCK)
  begin
  if(CLOCK ='1' and CLOCK'event)
  COUNT <= COUNT +1;
  end if;
  end process;

## Slide 49: Attributes
Signals change value while system is running
Understanding the signal information is possible using attributes
Example - Event attribute:
Signal’event
  Returns a Boolean value, that is True if a signal has events

## Slide 50: Example: 1-bit Register (D-type flip-flop)
DFF
D
CLK
Q
-- D type Flip Flop
entity dff is
port (D: in std_logic;
CLK: in std_logic;
Q: out std_logic);
end dff;
The input value (D) is transferred to the output (Q) only in the correspondence of an edge (for example rising edge) of the clock signal (CLK)

## Slide 51: Example: D-type flip-flop
architecture arch1 of dff is
begin
process (CLK)
  begin
  if (CLK ='1' and CLK'event) then
  Q <= D;
  end if;
  end process;
end arch1;

## Slide 52: Testbench
The simulation of a circuit requires a model of the circuit and a description of the stimuli to be applied
In VHDL this is accomplished using a testbench, i.e. a module:
  With no inputs and no outputs
  Including the system to be simulated
  Whose only functionality is to apply a proper set of stimuli with the desired timing
The testbenches are usually the only part of the VHDL code including temporal (non-synthesizable) statements
y <= "00" after 5s;

## Slide 53: Working principle
Device Under Test (Top Level)
Stimuli
entity testbench

## Slide 54: Developing a testbench
A testbench is usually the entity of higher level in a project
entity testbench1 is
end testbench1;
It will include the device to be tested as a component and as many signals as the inputs to be excited.
Implementation of a testbench:
  Connect declared signals to the inputs of the system under test using a port map
  Specify the temporal behaviour of the signals to obtain the sequences of desired inputs

## Slide 55: Simulation: general concepts
The simulation process allows the verification of the described circuit.
The simulation can be:
  A functional simulation, used to verify that the system effectively implements the desired functionality. This type of simulation requires the definition of an appropriate set of stimuli.
  A timing simulation, used to verify the (temporal) performance of the circuit. This type of simulation requires an opportune model of a platform, closely related to the selected hardware technology.

## Slide 56: HDL simulation
HDL simulators are Event Driven simulators
HDL represents hardware, that are composed of nodes that change logic values during the circuit work
Two concepts of time
  Delta Time
    Advances through multiple delta cycles
  Actual Time
    Advances through multiple time steps
The delta cycle is an HDL concept used to order events that occur in zero physical time

## Slide 57: HDL simulation
General HDL simulation: relation between delta cycles and time steps
  Whenever a signal changes, that signal output fans out to the input of other logic that may cause other signals to change. This happens over and over again and each iteration could be considered a delta cycle. The iteration stops when there are no more signals changing and then the simulator is ready to advance time with a time step.
Circles: signals updates
Squares: process evaluation

## Slide 58: Simulation tools
FPGAs Integrated Development Environments (IDE) usually include a simulation tool or support the use of external ones.
One of the best known simulation tools is ModelSim from Mentor Graphics.
  ModelSim versions are provided by Mentor Graphics and often integrated within manufacturers Design Suites.
An open source tool to consider: GHDL (Gnu HDL)

## Slide 59: Simulation tools
A simulation tool allows the verification (functional or timing) of a system given the set of input signals.
Besides testbenches, many simulators allow to manually specify the set of stimuli.
Waveform Generators are usually graphical interface tools that allow users to define with relative ease the timing diagrams of the input signals.

## Slide 60: Synthesis
Synthesis is the process of translating a description of a hardware system at higher abstraction level into an (optimized) implementation on a lower abstraction level.
  From HDL description to an implementation in terms of logic gates
FPGA manufacturers usually provide appropriate synthesis tool optimized for the target devices.
Not necessarily a simulated HDL model will be also synthesizable

## Slide 61: Synthesis tools
The synthesis tool must interpret VHDL constructs and translate them into the corresponding circuit implementation
The fundamental problem is to make sure that the translation process is correct (i.e. obtain the desired circuit)
A frequent problem example: undesired latches

## Slide 62: Constraints
Besides the model, the synthesis process is based also on constraints fixed by the user
Using the constraints, it is possible to try to obtain a certain behaviour of the synthesis tool, in order to optimize the final result
Most of the development environments supports the definition of the constraints by using dedicated files
  Example: Xilinx ISE User Constraints Files (.ucf)

## Slide 63: FPGA Internals
In a 7-series Xilinx FPGA
  2 slices per CLB (Configuration Logic Block)
  6-input LUTs, eight flip-flops and various multiplexers and arithmetic carry logic form a slice
CLB block diagram
Slice internal components

## Slide 64: - Xilinx ISE - Intel Altera - Xilinx Vivado (Homelab FPGA)
Tools for FPGA development

## Slide 65: Example: Greatest Common Divisor
int x, y;
while (1)
{
  while (!go_i);
  x = x_i;
  y = y_i;
  while (x != y)
  {
    if (x < y)
    y = y - x;
    else
    x = x - y;
  }
  d_o = x;
}
GCD
x_i
y_i
d_o
go_i
Calculus of the greatest common divisor between 2 numbers:
  The starting point is the algorithm description.

## Slide 66: GCD Calculator (Behavioural)
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity gcd1 is
port( Data_X: in unsigned(3 downto 0);
Data_Y: in unsigned(3 downto 0);
Data_out: out unsigned(3 downto 0)
);
end gcd1;

## Slide 67: GCD Calculator (Behavioural)
architecture behav of gcd1 is
begin
process(Data_X, Data_Y)
variable tmp_X, tmp_Y: unsigned(3 downto 0);
begin
tmp_X := Data_X;
tmp_Y := Data_Y;
for i in 0 to 15 loop
if (tmp_X /= tmp_Y) then
if (tmp_X < tmp_Y) then
tmp_Y := tmp_Y - tmp_X;
else
tmp_X := tmp_X - tmp_Y;
end if;
else
Data_out <= tmp_X;
end if;
end loop;
end process;
end behav;

## Slide 68: GCD Calculator (FSMD)
The algorithm is converted in a complex “finite state machine”
FSMD: finite-state machine with data

## Slide 69: GCD Calculator (FSMD)
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity gcd is
port( clk: in std_logic;
rst: in std_logic;
go_i: in std_logic;
x_i: in unsigned(3 downto 0);
y_i: in unsigned(3 downto 0);
d_o: out unsigned(3 downto 0)
);
end gcd;

## Slide 70: GCD Calculator (FSMD)
architecture FSMD of gcd is
begin
process(rst, clk)
-- define states using variable
type S_Type is (ST0, ST1, ST2);
variable State: S_Type := ST0 ;
variable Data_X, Data_Y: unsigned(3 downto 0);
begin
end process;
end FSMD;

## Slide 71: GCD Calculator (FSMD)
if (rst='1') then -- initialization
d_o <= "0000";
State := ST0;
elsif (clk'event and clk='1') then
case State is
when ST0 => -- starting
if (go_i='1') then
Data_X := x_i;
Data_Y := y_i;
State := ST1;
else
State := ST0;
end if;
when ST1 => -- idle state
State := ST2;

## Slide 72: Example: GCD Calculator (FSMD)
when ST2 => -- computation
if (Data_X/=Data_Y) then
if (Data_X<Data_Y) then
Data_Y := Data_Y - Data_X;
else
Data_X := Data_X - Data_Y;
end if;
State := ST1;
else
d_o <=Data_X; -- done
State := ST0;
end if;
when others => -- go back
d_o <= "ZZZZ";
State := ST0;
end case;
end if;

## Slide 73: GCD Calculator (FSM + DP)

## Slide 74: GCD Calculator (FSM + DP)
entity mux is
port( rst: in std_logic;
sLine: in std_logic;
load : in std_logic_vector( 3 downto 0 );
result: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 3 downto 0 )
);
end mux;
MULTIPLEXER (ENTITY)

## Slide 75: GCD Calculator (FSM + DP)
architecture mux_arc of mux is
begin
process( rst, sLine, load, result )
begin
if( rst = '1' ) then
output <= "0000"; -- do nothing
elsif sLine = '0' then
output <= load; -- load inputs
else
output <= result; -- load results
end if;
end process;
end mux_arc;
MULTIPLEXER (ARCHITECTURE)

## Slide 76: GCD Calculator (FSM + DP)
entity comparator is
port( rst: in std_logic;
x : in std_logic_vector( 3 downto 0 );
y: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 1 downto 0 )
);
end comparator;
COMPARATOR (ENTITY)

## Slide 77: GCD Calculator (FSM + DP)
architecture comparator_arc of comparator is
begin
process( x, y, rst )
begin
if( rst = '1' ) then
output <= "00"; -- do nothing
elsif( x > y ) then
output <= "10"; -- if x greater
elsif( x < y ) then
output <= "01"; -- if y greater
else
output <= "11"; -- if equivalence.
end if;
end process;
end comparator_arc;
COMPARATOR (ARCHITECTURE)

## Slide 78: GCD Calculator (FSM + DP)
entity subtractor is
port( rst: in std_logic;
cmd: in std_logic_vector( 1 downto 0 );
x : in std_logic_vector( 3 downto 0 );
y: in std_logic_vector( 3 downto 0 );
xout : out std_logic_vector( 3 downto 0 )
yout: out std_logic_vector( 3 downto 0 )
);
end subtractor;
SUBTRACTOR (ENTITY)

## Slide 79: GCD Calculator (FSM + DP)
architecture subtractor_arc of subtractor is
begin
process( rst, cmd, x, y )
begin
if( rst = '1' or cmd = "00" ) then -- not active.
xout <= "0000";
yout <= "0000";
elsif( cmd = "10" ) then -- x is greater
xout <= ( x - y );
yout <= y;
elsif( cmd = "01" ) then -- y is greater
xout <= x;
yout <= ( y - x );
else
xout <= x; -- x and y are equal
yout <= y;
end if;
end process;
end subtractor_arc;
SUBTRACTOR (ARCHITECTURE)

## Slide 80: GCD Calculator (FSM + DP)
entity regis is
port( rst, clk, load: in std_logic;
input: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 3 downto 0 )
);
end regis;
architecture regis_arc of regis is
begin
process( rst, clk, load, input )
begin
if( rst = '1' ) then
output <= "0000";
elsif( clk'event and clk = '1') then
if( load = '1' ) then
output <= input;
end if;
end if;
end process;
end regis_arc;
REGISTER

## Slide 81: GCD Calculator (FSM + DP)
component fsm is
port( rst, clk, proceed: in std_logic;
comparison: in std_logic_vector( 1 downto 0 );
enable, xsel, ysel, xld, yld: out std_logic
);
end component;
component mux is
port( rst, sLine: in std_logic;
load, result: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 3 downto 0 )
);
end component;
component comparator is
port( rst: in std_logic;
x, y: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 1 downto 0 )
);
end component;
GCD (ARCHITECTURE)

## Slide 82: GCD Calculator (FSM + DP)
component subtractor is
port( rst: in std_logic;
cmd: in std_logic_vector( 1 downto 0 );
x, y: in std_logic_vector( 3 downto 0 );
xout, yout: out std_logic_vector( 3 downto 0 )
);
end component;
component regis is
port( rst, clk, load: in std_logic;
input: in std_logic_vector( 3 downto 0 );
output: out std_logic_vector( 3 downto 0 )
);
end component;
signal xld, yld, xsel, ysel, enable: std_logic;
signal comparison: std_logic_vector( 1 downto 0 );
signal result: std_logic_vector( 3 downto 0 );
signal xsub, ysub, xmux, ymux, xreg, yreg: std_logic_vector( 3 downto 0 );
GCD (ARCHITECTURE)

## Slide 83: GCD Calculator (FSM + DP)
-- doing structure modelling here
-- FSM controller
TOFSM: fsm port map( rst, clk, go_i, comparison,
enable, xsel, ysel, xld, yld );
-- Datapath
X_MUX: mux port map( rst, xsel, x_i, xsub, xmux );
Y_MUX: mux port map( rst, ysel, y_i, ysub, ymux );
X_REG: regis port map( rst, clk, xld, xmux, xreg );
Y_REG: regis port map( rst, clk, yld, ymux, yreg );
U_COMP: comparator port map( rst, xreg, yreg, comparison );
X_SUB: subtractor port map( rst, comparison, xreg, yreg, xsub, ysub );
OUT_REG: regis port map( rst, clk, enable, xsub, result );
d_o <= result;
GCD (ARCHITECTURE)

## Slide 84: GCD Calculator (FSM + DP)
-- doing structure modelling here
-- FSM controller
TOFSM: fsm port map( rst, clk, go_i, comparison,
enable, xsel, ysel, xld, yld );
-- Datapath
X_MUX: mux port map( rst, xsel, x_i, xsub, xmux );
Y_MUX: mux port map( rst, ysel, y_i, ysub, ymux );
X_REG: regis port map( rst, clk, xld, xmux, xreg );
Y_REG: regis port map( rst, clk, yld, ymux, yreg );
U_COMP: comparator port map( rst, xreg, yreg, comparison );
X_SUB: subtractor port map( rst, comparison, xreg, yreg, xsub, ysub );
OUT_REG: regis port map( rst, clk, enable, xsub, result );
d_o <= result;
BAD DESCRIPTION STYLE !
GCD (ARCHITECTURE)

## Slide 85: GCD Calculator (FSM + DP)
-- doing structure modelling here
-- FSM controller
TOFSM: fsm port map(rst => rst,
clk => clk,
proceed => go_i,
comparison => comparison,
enable => enable,
xsel => xsel,
ysel => ysel,
xld => xld,
yld => yld
);
GCD (ARCHITECTURE)

## Slide 86: GCD Calculator (FSM + DP)
-- Datapath
X_MUX: mux port map( rst, xsel, x_i, xsub, xmux );
Y_MUX: mux port map( rst, ysel, y_i, ysub, ymux );
X_REG: regis port map( rst, clk, xld, xmux, xreg );
Y_REG: regis port map( rst, clk, yld, ymux, yreg );
U_COMP: comparator port map( rst, xreg, yreg, comparison );
X_SUB: subtractor port map( rst, comparison, xreg, yreg, xsub, ysub );
OUT_REG: regis port map( rst, clk, enable, xsub, result );
d_o <= result;
GCD (ARCHITECTURE)
DO THE SCHEMATIC

## Slide 87: GCD Calculator Testbench (FSMD)
entity test_GCD is
end test_GCD;
architecture Bench of test_GCD is
component gcd
port( clk: in std_logic;
rst: in std_logic;
go_i: in std_logic;
x_i: in unsigned(3 downto 0);
y_i: in unsigned(3 downto 0);
d_o: out unsigned(3 downto 0)
);
end component;
signal T_clk,T_rst,T_go_i: std_logic;
signal T_x_i, T_y_i, T_d_o: unsigned(3 downto 0);

## Slide 88: GCD Calculator Testbench (FSMD)
begin
U1: GCD port map(T_clk,T_rst,T_go_i,T_x_i,T_y_i,T_d_o);
Clk_sig: process
begin
T_clk<='1';
wait for 5 ns;
T_clk<='0';
wait for 5 ns;
end process;

## Slide 89: GCD Calculator Testbench – good description style
begin
U1: GCD port map
(clk => T_clk,
rst => T_rst,
go_i => T_go_i,
x_i => T_x_i,
y_i => T_y_i,
d_o => T_d_o
);
Clk_sig: process
begin
T_clk<='1';
wait for 5 ns;
T_clk<='0';
wait for 5 ns;
end process;

## Slide 90: Synthesis of GCD (FSMD)

## Slide 91: Synthesis of GCD (FSM + DP)

## Slide 92: Example: Embedded Processors

## Slide 93: Embedded Processors
Xilinx provides two types of processors for the development of embedded systems:
  Hard-processor: PowerPC (available in various models of Xilinx FPGAs) and ARM based processors, available on the Zynq-7000 devices
  Soft-processors: MicroBlaze, PicoBlaze
PowerPC and MicroBlaze are directly supported within the Embedded Development Kit and Vivado

## Slide 94: System Generator
System Generator is a development environment for FPGA-based digital signal processing architectures
  Simulink-based tool, supports the use of all Simulink features
  Large number of DSP blocks immediately available
  Possibility of exploiting Matlab to generate vectors of stimuli
System Generator also supports hardware co-simulation
Intel also provides a similar tool (DSP Builder)

## Slide 95: References
ANSI/IEEE Std 1076
Frank Vahid and Tony Givargis, Embedded System Design: A Unified Hardware/Software Introduction. John Wiley & Sons, 2002
Peter J. Ashenden, The Designer's Guide to VHDL, Morgan Kaufmann Publishers, 2008
Volnei A. Pedroni, Circuit Design and Simulation with VHDL - 2nd Edition, MIT Press, 2010
Pong P. Chu, RTL Hardware Design using VHDL, Wiley, 2006
Pong P. Chu, FPGA Prototyping by VHDL Examples: Xilinx Spartan-3 Version, Wiley, 2008

## Slide 96: Free & open resources
vhdl.org
OpenCores: open source hardware resource
Vendors websites: Xilinx (forum recommended), Altera
GHDL: GPL VHDL Simulator
ActiveHDL: simulator and various tutorials
Cobham Gaisler: Leon 3 processor
SIGASI Insights: VHDL's crown jewel
SIGASI Insights: Verilog's major flaw

## Slide 97: Thank you !
Contact: giacomo.valente@univaq.it