## Slide 1: Transaction Level Modeling with SystemC
Sonali Dutta
September 23, 2011

## Slide 2: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 3: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 4: Abstraction Levels
TLM
Cycle Accurate
RTL
Gate
Layout
Functional
Abstraction
Automated Translation
Manual Translation
Traditional hardware Design Process
Synthesis
PnR

## Slide 5: Shortcomings of Traditional Design
Simulation speed
Simultaneous development of software
Time-to-market
Cost
3

## Slide 6: Solutions
Hardware Emulation
  Waits for RTL
  Very costly
  Limited debugging capabilities

## Slide 7: Solutions
Hardware Emulation
Cycle Accurate Model
  Limited speed up
  Significant modeling effort
  Hard to cope up with RTL evolutions

## Slide 8: Solutions
Emulation
Cycle Accurate Model
TLM
6

## Slide 9: Simulation Time for encoding and decoding a MPEG 4 frame
1
10
100
1000
Hardware Emulation
TLM
RTL + co simulation
RTL
1 hour
3 minutes
3 seconds
1 second
1200 times
Simulation time(s)
(logarithmic scale)

## Slide 10: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 11: TLM Overview
What is TLM?
  Communication uses function calls
  Emphasis more on what data is transferred where
  Implementation detail like actual protocol is abstracted
Types of Communication
  Interrupt – unidirectional point to point communication
  Transaction – data exchange between initiator/master and target/slave

## Slide 12: Generic TL Channel: A building block
The generic channel is a building block that
eases implementing data passing and
synchronization of initiator and target.
INITIATOR
TARGET
CHANNEL
It is not ready made implementation of any communication protocol.

## Slide 13: Example TLM platform
Processor
Memory
Interrupt Controller
Direct Memory Access Controller
Timer
Bus
Initiator port
Target port
Interrupt Input
Interrupt output

## Slide 14: Memory Address Map
ROM
DMAC
Timer
RAM
Interrupt Controller
0x00000000
0x03FFFFFF
0x10000000
0x10100000
0x101000FF
0x20000000
0x23FFFFFF
0x30000000
0x3000000F
0x100000FF
The interconnection network routes the transactions depending on a global address map.
The global address map associates each target with a memory range.

## Slide 15: Contract between embedded software and hardware
For the embedded software to run correctly :
  Register Accuracy: The address map, the offset for each register must be the same as in the final chip.
  Data Accuracy: The data produced and exchanged by the components must also be the same with the final chip.
  The interrupts have to correspond logically to the final ones.

## Slide 16: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 17: Producer Consumer Communication
Producer
Consumer
Clock Signal
Value Signal
clock
value
clock
value

## Slide 18: Producer
  struct Producer : public sc_module
  {
  //Ports
  sc_out<bool> clock;
  sc_out<int> value;
  SC_HAS_PROCESS ( Producer);
  Producer (sc_module_name name) : sc_module (name)
  {
  //declares compute as a thread
  SC_THREAD (compute);
  }
  void compute()
  {
  for (int i=0; i<10; ++i)
  { clock.write (false);
  wait (10, SC_NS); //waits for 10 nanoseconds
  clock.write (true);
  value.write(i);
  wait (5, SC_NS); //wait for 5 nanoseconds
  }
  }
  };

## Slide 19: Consumer
    struct Consumer : public sc_module
    {
    //ports
    sc_in <bool> clock;
    sc_in <int> value;
    SC_HAS_PROCESS (Consumer);
    Consumer (sc_module_name name) : sc_module (name)
    { //declares receive() as a process triggered on clock value changes
    SC_METHOD(receive);
    sensitive << clock;
    }
    void receive()
    {
    //if clock is changing from false to true
    if (clock.posedge ())
    {
    std::cout << “Received: “ << value.read() << std::endl;
    }
    }
    };

## Slide 20: TLM Communication Scheme
An initiator uses a process to perform its communication.
A target is inherently always ready to receive a communication.
The function call blocks the initiator process until the communication finishes(after the implementation of the function in the target returns).

## Slide 21: TLM Communication Scheme
INITIATOR
TARGET
Channel
Void function(…)
{
…
}
P
function()
function()
function()

## Slide 22: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 23: Simple Bus Modules
Masters: initiate transactions on the bus.
  Ex: CPUs, DSPs
Slaves: respond to bus requests.
  Ex: ROMs, RAMs, I/O devices
Bus: connects the masters and the slaves and allow them to communicate using bus transactions.
Arbiter: used by the bus to select a request to execute from the competing bus requests.
Clock Generator: provides a clock signal to synchronize.

## Slide 24: Block diagram of Simple Bus
Blocking master
Non blocking master
Direct master
Bus
Fast slave
Slow slave
Arbiter
Interface
port
Global clock
I1
I2
I3
I4
I4
I5
I1: Blocking Master Interface
I2: Non blocking Master Interface
I3: Direct Master Interface
I4: Slave Interface
I5: Arbiter Interface

## Slide 25: Blocking Master Interface
class simple_bus_blocking_if :
public virtual sc_interface
{
public:
virtual simple_bus_status burst_read(
unsigned int unique_priority,
int *data,
unsigned int start_address,
unsigned int length,
bool lock)=0;
virtual simple_bus_status_burst_write(
unsigned int unique_priority,
int *data,
unsigned int start_address,
unsigned int length,
bool lock)=0;
};

## Slide 26: Non Blocking Master Interface
class simple_bus_non_blocking_if :
public virtual sc_interface
{
public:
virtual void read(
unsigned int unique_priority,
int *data,
unsigned int address,
bool lock)=0;
virtual void write(
unsigned int unique_priority,
int *data,
unsigned int address,
bool lock)=0;
virtual simple_bus_status get_status(
unsigned int unique_priority)=0;
};

## Slide 27: Direct Master Interface
class simple_bus_direct_if :
public virtual sc_interface
{
public:
virtual bool direct_read(
int *data,
unsigned int address)=0;
virtual bool direct_write(
int *data,
unsigned int address)=0;
};

## Slide 28: Slave Interface
class simple_bus_slave_if :
public virtual sc_interface
{
public:
virtual simple_bus_status read(
int *data,
unsigned int address)=0;
virtual simple_bus_status write(
int *data,
unsigned int address)=0;
virtual unsigned int start_address(
) const =0;
virtual unsigned int end_address(
) const =0;
};

## Slide 29: Arbiter Interface
class simple_bus_arbiter_if :
public virtual sc_interface
{
public:
virtual simple_bus_request*arbitrate(
const simple_bus_request_vec &requests)=0;
};

## Slide 30: Overall Execution Scheme within Simple Bus
BUS
(a set of outstanding requests)
Masters
Slaves
Arbiter
(Arbitration rules)
1
Request
Vector of requests
2
3
Selected request
4
Request
5
Read/write(indication of wait)
Reissue if wait
6
7
Request complete
8
Update status
25

## Slide 31: Outline
Need for higher abstraction
TLM overview
Producer Consumer Model Example
Simple Bus Example
TLM Applications

## Slide 32: TLM Applications
Development and execution of embedded software.
Functional verification of the hardware block
Serves as tool of communication among software developers, RTL modelers and verification team.
Evaluation of chip performance to determine the best compromise between area, cost , speed etc.

## Slide 33: Thank You Q&A